## Slide 1: Lab#11: Serial Dilutions & Quantification of Fecal Coliform Bacteria

## Slide 2: Purpose: Quantification of Fecal Coliform Bacteria
Fecal coliform bacteria are found in the intestinal tract of all warm-blooded animals. Each discharge of body wastes contains large amounts of these organisms.
The presence of fecal coliform bacteria in a stream or lake water indicates the presence of human or animal wastes.
The large number of fecal coliform bacteria present is also a good indicator of the presence of other disease-producing organisms in the water.
For this reason, regulatory agencies with responsibility for protection of public health have established water quality standards, which include maximum levels of fecal coliform bacteria.
Fecal coliform is measured in colony forming units per 100 mL, CFU/100 mL, of water tested.

## Slide 3: Purpose: Serial Dilution
The number of bacteria in a given sample of water is usually too high to be counted directly.
However, if the sample is serially diluted and then plated out on an agar plate in such a manner that single isolated bacteria form visible isolated colonies, the number of colonies can be used as a measure of the number of viable cells in the original water sample.
In microbiology, serial dilutions are used to decrease a bacterial concentration to a required concentration which is easier to count when plated to an agar plate.

## Slide 4: Serial Dilution
A serial dilution is a series of sequential dilutions used to reduce a dense culture of cells to a more usable/countable concentration. Each dilution will reduce the concentration of bacteria by a specific amount. So, by calculating the total dilution over the entire series, it is possible to know how many bacteria were there in the original sample.
Normally, the bacterial sample is diluted by factors of 10 and plated on agar.
After incubation, the number of colonies on a dilution plate showing between 30-300 colonies is determined.
A plate having 30-300 colonies is chosen because this range is considered statistically significant.

## Slide 5: Serial Dilution
3 Plate picture that can be counted or not (This plate has over 300 colonies and can not be used for counting; This plate has between 30-300 colonies and is a suitable plate for counting; This plate has less than 30 colonies and is unusable for counting)

## Slide 6: Materials Needed
Sample of lake/drinking water
Eight 9-ml water blanks per team
Eight agar plates per team
Ten sterile disposable 1ml pipettes per team
Spreading rods
Vortex machine

## Slide 7: Procedure: Serial Dilution
Each group will get a sample of lake water collected from a nearby source and use the techniques learned to perform a set of serial dilutions and spread plates for the sample.
1. Using you sample, transfer 1ml into the first sterile water blank. Label this tube 1:10.
2. Mix the tube contents using the vortex mixer on the end of each table.
3. Using another transfer pipette, transfer 1ml of the 1:10 tube to the next sterile blank tube. Label this tube 1:100.
4. Continue making transfers until 1:100 and 1:10000 dilutions have been made.
5. After all dilution have been completed, Transfer . ml from the original sample and place it on a plate labeled 1:1
6. Then, transfer 1/2 ml from the 1:10 dilution tube and place it on a plate labeled 1:10.
7. Spread the liquid across the surface of the plate with a clean spreading rod.
8. Continue making plates in this fashion from each of the dilution tubes until you have created five plates: 1:1, 1:10, 1:100, 1:1000, 1: 10,000
9. Place the inverted plates in a rack to be incubated.

## Slide 8: Procedure: Serial Dilution
10 ml tube
10 ml tube
10 ml tube
10 ml tube
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
9 ml H2O
9 ml H2O
9 ml H2O
9 ml H2O
stock

## Slide 9: Procedure: Serial Dilution
stock
10 ml tube
1:10
10 ml tube
10 ml tube
10 ml tube
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
1ml
9 ml H2O
9 ml H2O
9 ml H2O
9 ml H2O

## Slide 10: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
10 ml tube
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
1ml
9 ml H2O
9 ml H2O
9 ml H2O
stock

## Slide 11: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
1:1,000
10 ml tube
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
1ml
9 ml H2O
9 ml H2O
stock

## Slide 12: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
1:1,000
10 ml tube
1:10,000
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
1ml
9 ml H2O
stock

## Slide 13: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
1:1,000
10 ml tube
1:10,000
Agar plate
Agar plate
Agar plate
Agar plate
Agar plate
stock

## Slide 14: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
1:1,000
10 ml tube
1:10,000
Agar plate
1:1
Agar plate
1:10
Agar plate
1:100
Agar plate
1:1,000
Agar plate
1:10,000
stock
0.5 ml
0.5 ml
0.5 ml
0.5 ml
0.5 ml

## Slide 15: Procedure: Serial Dilution
10 ml tube
1:10
10 ml tube
1:100
10 ml tube
1:1,000
10 ml tube
1:10,000
Agar plate
1:1
Agar plate
1:10
Agar plate
1:100
Agar plate
1:1,000
Agar plate
1:10,000
stock

## Slide 16: Spread Plate Counts
A colony is the result of rapid division of one or a few cells giving rise to a visible mass.
Count the number of colonies growing on the plates to determine the number of colonies/bacteria in ½ ml of the diluted solution
Then a calculation of the viable cells in the original sample can be performed.

## Slide 17: How to Calculate Dilution Factor
To calculate the dilution factor, you need two things: the original volume of the solution you have added to dilute (Vi)and the final volume after diluting (Vf=the original volume plus the volume you have added).
The dilution factor or the dilution is the added sample volume divided by the final volume.
      DF=Vi/Vf
For example, if you add 1 mL sample to 9 mL of diluent to get 10 mL of solution, then
      DF=Vi/Vf = 1mL/10mL=1/10. This is a 1:10 dilution.
Remember that serial dilutions are always made by taking a set quantity of the initial dilution and adding it successively to tubes with the same volume. So you multiply each successive dilution by the dilution factor.
The dilution factor after four dilutions is
      DF=(1/10) × (1/10) × (1/10) × (1/10) =1/10,000 = 1:10,000

## Slide 18: Calculation of CFU/ml of Original Sample
Formula:
CFU/ml of original sample= number of colonies/ (dilution factor X volume of sample plated on each agar plate)
Example: If the 1:100 plate shows 148 living colonies, and volume of sample-water plated on each agar plate was ½ ml, then
CFU/ml of original sample= 148/ (1/100) X ½ = 148 X 100 X 2 = 29,600
Therefore,
in 100 ml of the original sample= 29,600X 100 CFUs = 29,600,00 CFUs

## Slide 19: Result
Number of colonies counted in your sample | Number of colonies in Group 2’s sample | Number of colonies in Group 3’s sample | Number of colonies in Group 4’s sample | Average number of colonies counted | CFUs
US EPA Permissible level (CFU/100mL) | 
Drinking Water | 0
Swimming | < 1,000
Boating or Fishing | < 4,000