## Slide 1: Lab #2: Microscopy

## Slide 2: Compound Light Microscope
MICROSCOPE: Is an instrument for viewing objects that are too small to be seen by the naked or unaided eye.
MICROSCOPY: The science of investigating small objects using such an instrument is called microscopy
Compound microscope has two sets of lenses for magnification.
    Lenses closer to the eye = Ocular lens
    Lenses closer to the object being viewed = Objective lens.
    Microscope used in Microbiology lab has four objective lenses.

## Slide 3: Basic Parts of a Microscope
Ocular lens – Closest to your eyes; where you look into; has a lens that can magnify up to 10x
Body - tube that connects the eyepiece to the objective lenses
Arm – used for handling and supporting the microscope
Nosepiece – rotating part that holds all objective lenses
Objective lenses – primary image formation is done by these lenses; catches the light and magnifies the specimen
Condenser- a lens, just below the stage; gathers all the light coming from the illuminator; light is then focused through the object and magnified by the objective lens.
1
2
3
5
7
8
4
6
11
12
13

## Slide 4: Basic Parts of a Microscope Part II
7. Diaphragm – Controls the amount of light going through the condenser to the specimen
8. Mechanical Stage – Platform where slides are placed
9. Stage clips – Hold the slides in place
10. Illuminator – Light source, which can either be a mirror or a light bulb depending on the type of microscope
11. Coarse Adjustment Knob – Moves the stage nearer or farther from the objective lens; used for focusing at a lower power
12. Fine Adjustment Knob – Used to clear out the image
13. Base – bottom of the microscope that supports all the other parts

## Slide 5: The Ocular Lenses
Magnifies the specimen 10x
Based on the individual face width, the ocular lenses should be moved in relationship to each other and adjusted, so that one lighted circle (field of view) is seen simultaneously with both left and right eyes.
Left ocular is adjustable, and it is possible to adjust the ocular lenses to accommodate the difference of vision between the right and left eyes. This will allow viewing without the use of eyeglasses.
  If you use lens or glass- set it on 0. or,
  Use only the right ocular while focusing with the coarse-adjustment, then use the fine focus to make the object clear.
  Using the left ocular alone, turn the numbered dial at the base of the left ocular until the image is clear.
  Look through both oculars.

## Slide 6: Magnification and Objective Lenses
Rotary nosepiece of microscope has four objective lenses attached.
To calculate the power of magnification, multiply the power of the ocular lens by the power of the objective lens.
Scanning Power Objective Lens:
Red band around it.
Magnifies objects 4x.
What is the Total Magnification? ____

## Slide 7: Magnification and Objective Lenses
Low Power Objective Lens:
Has yellow band around it.
Magnifies objects 10x.
What is the Total Magnification? ____
What does the term parfocal mean?
High Dry Objective Lens:
Has blue band around it.
Magnifies objects 40x.
What is the Total Magnification? ____

## Slide 8: Magnification and Objective Lenses
Oil Immersion Lens:
Has the highest magnification power, 100X
Total magnification ?___________.
To improve resolution and use of light, an oil of the same refractive index as the glass slide and the objective lens is placed between the two.
Oil prevents refraction of light outwards and allows it to pass straight into objective.

## Slide 9: How To Focus
Adjust the ocular lenses to see through one lighted circle (field of view).
Place the prepared slides on the mechanical stage, securing it with stage clips.
Adjust diaphragm and light source to get light. At the beginning, you need very little light. Keep diaphragm completely open but adjust the rheostat.
Check Condenser: Needs to be pretty close to the stage, just 1-2 mm below the slide.
Rotate the nosepiece to click the red-banded Low objective (4x) on place.

## Slide 10: How To Focus Part II
Use the coarse adjustment knob (large knob) to take the stage at the lowest position and then slowly bring it up. Continue until you get the image into view (to be sure, move the stage up/down at least 2/3 times)
Use the fine adjustment knob (small knob) to make the image clearer to see more detail.
Adjust the slide so you can see the specimen in the center.
Once you have the image in view, rotate the nosepiece to view it under different powers
Start at the lowest magnification, then work your way up. Fine focusing on different levels is necessary so you can choose the clearest view.
Adjust the diaphragm when you move from one magnification level to another. A higher magnification may require more light than the lower objectives.

## Slide 11: How To Focus Part III
Oil Immersion Lens: Put just one drop of oil only when 100X are on place
If you can not see the image anymore, do not go back to 40X (Dry-high) and 10X!!!!!
Can go back to 4X
Do not use Camp wipe to clean lens. Use lens paper to clean lens. Do not mop. Just DAB DAB DAB (4/5 times)
Use camp wipe to clean the slide.

## Slide 12: Take Care of Your Scope
Getting Scope Out:
When moving your scope, always hold it with one hand under the base, and one hand around the arm.
Pick up the scope and gently put it down in front of you. Never scoot it because the vibration caused by the nonskid bottom of the scope on the lab bench can damage the scope.
Before you turn on switch for light - make sure to turn the knob (Rheostat) towards the lowest light, otherwise bulb will break. Then turn on the switch and increase the light intensity.
Putting Scope Away:
  Use lens paper to clean lenses. Do not use the same lens paper to clean other lenses.
  If observing several slides with oil in sequence, the oil-immersion lens does not need to be cleaned between each slide.
  Clean stage if it is oily with kim-wipes
  Use course focus to position stage as low as it can go.
  Shortest objective lens (the one with the red band) should be pointing down toward stage.
  Always put scope back in the scope cabinet.