## Slide 1: Lab#4: Bacterial Transfer and Sterile Technique

## Slide 2: Bacterial Transfer
While transferring the cultures of living organisms into new media, it is essential to follow a procedure, known as ‘Aseptic (sterile) Technique.’
The goals of this procedure are twofold:
  to greatly minimize, or even to eliminate the risk of contamination of the culture
  to prevent spread of culture organisms to the lab personnel or the environment.

## Slide 3: Sterile vs. Aseptic
Sterile means absence of all microorganisms.
Aseptic does not eliminate all microorganisms but eliminates the possibilities of contamination from unwanted microorganisms and ensures that none will be introduced into the sample.

## Slide 4: 3 Forms of Media
There are 3 forms of media:
  An agar medium contains agar (1.5-2%) as a solidifying agent---isolation and purification.
  A broth medium has no agar: it is for fast, luxuriant growth.
  A semi-solid has a reduced percentage of agar, and, therefore, has qualities of both types.

## Slide 5: Culture Medium
Culture Medium: Culture medium or growth medium is a liquid broth, or a solid agar slant or plate designed to support the growth of microorganisms.
The most common growth media are Tryptic soy agar (TSA) and Tryptic soy broth.
A particular medium may be designed to contain only the minimum requirements for growth of a specific organism. This is “ minimal media” for that organism
  Enriched media- Some fastidious organisms need specialized environments due to complex nutritional requirements. Ex: Blood agar plate for Streptococcus sp.
  Typically, common organisms are grown on a standardized beef extract or protein base containing requirements for most bacterial species. Nutrient media and tryptic soy media are examples.

## Slide 6: Stock and Pure Culture
Stock Culture: Cultures of microorganisms that are stored or maintained for future use in such a fashion that their growth and productive capacities remains unaltered.
Pure Culture: Only one species of organism in the culture.

## Slide 7: Materials Needed
Bacti-cinerator
Inoculating loop
TSA plate cultures of Staph epidermidis, Bacillus subtilis, and E.coli
TSB (trypticase soy broth) cultures of Staph epidermidis, Bacillus subtilis, and E.coli
6 TSB
1 marker pen or grease pencil
Labelling tape
Tube and plate racks

## Slide 8: Procedure (Broth to Broth Transfer)
  First, label the tubes with the following information: Name, date, and the name of organism to be inoculated.
  Place the tubes in a rack and turn on the Bacti-Cinerator. Warm-up time for Bacti-cinerator is about ten minutes.
  Choose a stock culture and a correspondingly labeled sterile tube. Hold both in the left hand, with the culture closest to you. (Reverse these instructions if you are left-handed).
  Loosen the caps until they will just lift off. Do not uncover the tubes at this point.

## Slide 9: Procedure (Broth to Broth Transfer) Part II
  Hold the inoculation loop in your right hand.
  Insert the inoculation loop into the chamber briefly for 8-10 seconds to heat-sterilize it.
    Do not leave your loop in the incinerator for more than 10 seconds, you will destroy the loop!
  Give little time (about 10 seconds) for your loop to cool.
  Crook the little finger (Pinky) of the right hand around the cap of the stock culture, then lift the cap and secure it with the pinky.
  Secure the cap of the sterile tube same way with the third or fourth finger of your right hand.
    Never put the caps down on the lab table, this would contaminate the caps and the lab table.
    Keep the caps in place between your fingers, taking care not to palm them or turn them up.

## Slide 10: Procedure (Broth to Broth Transfer) Part III
Stock tube held
by thumb near body
Sterile tube is held
far from the body

## Slide 11: Procedure (Broth to Broth Transfer) Part IV
Crook the little finger of the right hand around the cap of the stock culture
Crook the third or fourth finger around the cap of the sterile tube.

## Slide 12: Procedure (Broth to Broth Transfer) Part V
  Sterilize the neck/tops of the tubes (Stock and sterile) by passing them through the mouth of the Bacti-Cinerator 2-3 times.
  This hits the air at the neck of the tubes so that environmental organisms do not fall into and contaminate the tubes.
  Insert the now-cooled loop just below the surface of the stock culture and carefully withdraw the inoculating loop without touching the sides of the tube.
  As you pull it back out, you will notice a film (like soap bubbles) across the loop. This sample is referred to as the inoculum.
Now insert it into the sterile broth tube.
  Lower the loop below the surface, shake gently, and withdraw as before without touching the sides of the tube.

## Slide 13: Procedure (Broth to Broth Transfer) Part VI
  Flame the mouth of your tubes again, and replace the caps
    Do not miss your caps
  Heat-sterilize the loop. Place your loop in the mouth of the incinerator.
  Tighten the caps of the tubes fully, then loosen by one turn and return the tubes to the rack for incubation at 37°C . The cultures will be incubated for 48 hours.

## Slide 14: Procedure (Solid to liquid Transfer) Part I
  First, label the tube with the following information: Name, date, and the name of organism to be inoculated.
  Place the tube in a rack and turn on the Bacti-Cinerator. Warm-up time for Bacti-cinerator is about ten minutes.
  Hold the inoculation loop in your right hand
  Insert the inoculation loop into the chamber briefly for 8-10 seconds to heat-sterilize it.
    Do not leave your loop in the incinerator for more than 10 seconds, you will destroy the loop!
  Wait about 10 seconds for your loop to cool.

## Slide 15: Procedure (Solid to liquid Transfer) Part II
  Lift the lid of the plate with the bacteria just a bit, in order to get your inoculating loop into it.
    Do not take the entire lid off!
  Gently touch the loop to a single isolated colony on a stock agar plate and scoop up only one colony or a bit of a colony, if big, with your loop. This sample is referred to as the inoculum. Close the lid of the plate
  Grasp the lid off the sterile tube and flame the mouth using the Bacti-cinerator.
  Insert the loop into the broth without touching the sides of the tube. Twirl the loop like a swizzle stick to dislodge the bacteria

## Slide 16: Procedure (Solid to liquid Transfer) Part III
Touch the loop to the side of the tube by the mouth to remove excess fluid.
Use the incinerator to sterilize the loop.
Flame the mouth of the tube with the Bunsen burner and replace the cap.
Place your labeled broth tube in the rack for incubation. Incubate at 37°C for 24 hours.
You will check them next lab period for growth.

## Slide 17: Things to Remember
Flame loop until it turns orange
Flame lip of tube after you open it and right before you close it
The inoculum is obtained by first shaking the culture a bit, and then going into the broth with the loop.
Remove cap of tubes with same hand that is holding the loop (use pinky/little finger for stock culture, 3rd /4th finger for sterile culture)
Only open plates/tubes when you have to (never leave open unnecessarily)
If loop has not cooled enough before touching broth or agar, a sizzling sound will be heard. This produces aerosols of living bacteria, which contaminate the environment, and can reduce the chance of viability of the transferred specimen.