## Slide 1: Open educational resources for introduction to geographic information systems funded by: USG affordable learning grant
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Department of Geography and Anthropology
Module 2
Spatial Data Fundamentals

## Slide 2: Overview
Geospatial Data Models
  Objects and Attributes
Types of Spatial Phenomenon
  Discrete
  Continuous
  Organizing Geospatial Data Models – Attributes
Spatial Data Models
  Vector
  Raster

## Slide 3: Summary
This module focuses on geospatial data models. You will learn about discrete and continuous spatial phenomena and how these concepts are applied in mapped examples. The module will briefly introduce attributes, but they will also be covered in more detail in a future module. Lastly, this module covers the differences between the vector and the raster data model.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 4: Geospatial data models
A geospatial data model is a formal means of representing spatially referenced information.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 5: Objects and attributes
The object in geospatial data stores the geometry of the spatial phenomenon that is being modeled.
The attribute stores the descriptive information related to the object part of the geospatial data model.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 6: Discrete Data
Also called thematic, categorical, or discontinuous data.
A discrete object has known and definable boundaries.
It is easy to define precisely where the object begins and where it ends.
Examples: counties, light poles, lakes, etc.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 7: Continuous Data
Also referred to as field, non-discrete, or surface data.
A continuous surface represents phenomena in which each location on the surface is a measure of the concentration level or its relationship from a fixed point in space or from an emitting source.
Examples: elevation, soil type, rain fall, etc.
Used more commonly in environmental applications.
Notes: Based on measurement, estimate, or interpolation.

## Slide 8: ORGANIZATION OF SPATIAL DATA
Generally spatial phenomena are organized into separate geospatial data models by theme.
Example of the Mexico map with 5 layers:
  Cities
  Water
  Roads
  State boundaries
  National boundary
Notes: Based on measurement, estimate, or interpolation.

## Slide 9: Vector Data Vs. Raster Data

## Slide 10: Which layers are vector and which are raster?
ESRI.com

## Slide 11: Vector vs. Raster Data Model
ESRI.com

## Slide 12
Bruce Davis – GIS: A Visual Approach
Vector vs. Raster Data Model

## Slide 13: Spatial Data Models
Vector Data Model – better for displaying discrete objects
Raster Data Model – better for displaying continuous data
Notes: The vector data model is more suited to the question of “What do I know about this geographic feature?” The raster data model answers the question “What geographic phenomenon occurs at this location?”

## Slide 14
Points: A combination of two numbers [X-Y or Lat-Long] that represent locations with zero dimensions.
e.g. Wells, Crime scenes, Cities, Electric Poles
Lines: The shortest distance connecting 2 points --
lines have a beginning and an ending point, and
therefore a left and right side. Lines may also have vertices between the beginning and ending points, and are represented as strings of X-Y coordinate pairs.
e.g. Roads, Streams, Pipelines, Shorelines
Polygons: A set of points connected by line segments that close back to the first vertex, being represented by a closed loop of X-Y coordinate pairs. By definition, a polygon cannot contain intersections.
e.g. Lakes, Building Footprints, Census Tracts
Points
Lines
end
vertices
start
Vector GIS Feature Types
Polygons
Notes: Points are the fundamental and simplest form of geographical objects and are zero-dimensional because they have no extension. Each point is represented by a coordinate pair. A point has no boundary.
Lines consist of points linked together with line segments. The points, represent start, break, or end points of the line. Lines are one-dimensional, as they stretch in only one direction. Two is the lowest number of coordinate pairs representing a straight line between two points.
Area: An area is represented by a single line that encloses a space thus forming a closed polygon. The surrounding line, called a ring, has to start and end at the same point in order for the area to be closed and defined. Areas are two-dimensional because they stretch in 2 dimensions. The term polygon is often used to designate an area. Areas is the most complicated of the geometric primitives. It is possible to have complex areas with different variants of inner rings defining holes, and holes in holes. Thus, an area has a closed line in the outer boundary, but can also have several inner boundaries.

## Slide 15: What is Raster Data?
In its simplest form, a raster consists of a matrix of cells (or pixels) organized into rows and columns (or a grid) where each cell contains a value representing information, such as temperature.
Examples of rasters are:
  digital aerial photographs
  imagery from satellites
  digital pictures
  scanned maps
  etc.
Notes: The raster model represents reality through selected surfaces arranged in a regular pattern. The raster model is in many ways a mathematical model, as represented by the regular cell pattern. Because squares or rectangles are often used and a pictorial view of them resembles a classic grid of squares, it is sometimes called the grid model. Geometric resolution of the model depends on the size of the cells.

## Slide 16: Raster Representation
Real world
Grid
Raster
Column
Row
Notes: Reality is generalized in terms of uniform, regular cells, which are usually rectangular or square but may triangular or hexagonal.
The cells of a model are given in a sequence determined by a hierarchy of rows and columns in a matrix, with numbering usually starting from the upper left corner (Figure 4.20). The geometric location of a cell, and hence the object it represents, is stated in terms of its row and column numbers. The cells are often called pixels (picture elements), a term borrowed from the video screen technology used in TV and computer displays. A pixel is the smallest element of an image that can be processed and displayed individually.

## Slide 17: Raster Representation
Real world
Grid
Raster
Point
Line
Area
Value
=0
=1
=2
=3
Notes: Reality is generalized in terms of uniform, regular cells, which are usually rectangular or square but may triangular or hexagonal.
The cells of a model are given in a sequence determined by a hierarchy of rows and columns in a matrix, with numbering usually starting from the upper left corner (Figure 4.20). The geometric location of a cell, and hence the object it represents, is stated in terms of its row and column numbers. The cells are often called pixels (picture elements), a term borrowed from the video screen technology used in TV and computer displays. A pixel is the smallest element of an image that can be processed and displayed individually.

## Slide 18: Raster Representation
Triangles
Hexagons
Pixels are most commonly squares, but can also be other shapes.
Notes: Reality is generalized in terms of uniform, regular cells, which are usually rectangular or square but may triangular or hexagonal.
The cells of a model are given in a sequence determined by a hierarchy of rows and columns in a matrix, with numbering usually starting from the upper left corner (Figure 4.20). The geometric location of a cell, and hence the object it represents, is stated in terms of its row and column numbers. The cells are often called pixels (picture elements), a term borrowed from the video screen technology used in TV and computer displays. A pixel is the smallest element of an image that can be processed and displayed individually.

## Slide 19: Vector and Raster
Real World
Vector Representation
Raster Representation
line
polygon
point

## Slide 20: Points
A point is represented by an explicit x, y coordinate in vector format, but as a raster, it is represented as a single cell—the smallest unit of a raster.
By definition, a point has no area but is converted to a cell representing area. Therefore, the smaller the cell size, the smaller the area and, thus, the closer the representation of the point feature.
For example, it is assumed that a well, a telephone pole, or the location of an endangered plant occupies the entire area covered by a cell.
Vector Point Feature
Raster Point Feature
Notes: With a cell representation of point data, there is some generalization of the original data. In general, if two or more points fall within the extent of a cell, the GIS program randomly selects one of the points when assigning a value to the cell.
Point data features will become the size of the cell. Thus, you should choose a cell size appropriate to the feature that the point represents. You should make your cell size small enough to capture enough of the input points for the desired analysis.

## Slide 21: Lines
In vector format, a line is an ordered list of x, y coordinates, but in raster format it is represented as a chain of spatially connected cells with the same value.
Vector Line Feature
Raster Line Feature
Notes: Converting linear data to a raster dataset is similar to converting point data to a raster.
For any line that passes within the extent of a cell, that cell will receive the value of the attribute identified in the conversion.
If multiple lines pass through a single cell, the GIS program will randomly select one of the lines to use to represent that cell location in the output raster dataset.
As with point data, linear features will become the width of the cell.
For example, if the linear features that are being converted represent roads and the cell size is one kilometer, the road will be one kilometer wide in the output raster dataset. Obviously, a road is not one kilometer wide; thus, you should choose a cell size that is appropriate to the linear feature that you are representing. If the cell size is one meter, the road would be one meter wide.

## Slide 22: Polygons
A vector polygon is an enclosed area defined by an ordered list of x, y coordinates in which the first and last coordinates are the same, thereby representing area. By contrast, a raster polygon is a group of contiguous cells with the same value that most accurately portray the shape of the area.
Polygonal, or area, data is best represented by a series of connected cells. Examples of polygonal features include buildings, ponds, soils, forests, swamps, and fields.
Vector Polygon Feature
Raster Polygon Feature
Notes: If the input data is polygonal, each cell on the resulting output raster dataset from the conversion process is assigned the value of the feature that fills the majority of the cell.

## Slide 23: Discrete vs. Continuous
Discrete example:
  Landuse
Continuous example:
  Elevation
Raster data is more commonly used for continuous data.

## Slide 24: Value Attribute Table
Value | Count | Category | Code
1 | 124 | CBD | CBD
2 | 145 | Comm 1 | C – 1
3 | 107 | Comm 2 | C – 2
4 | 117 | Industrial | I
5 | 142 | Multifamily | MF
6 | 91 | Single Family – Attached | SFA
7 | 206 | Single Family - Detached | SFD
8 | 175 | Townhomes | T
VAT:
Notes: For discrete data

## Slide 25: Cell Values
Cell values can be either:
  positive
  negative
  integer - best used to represent categorical (discrete) data
  floating point (decimals) - to represent continuous surfaces

## Slide 26: NoData Values
Cells can also have a NoData value to represent the absence of data.

## Slide 27: Cells
The area (or surface) represented by each cell consists of the same width and height and is an equal portion of the entire surface represented by the raster.
For example, a raster representing elevation may cover an area of 100 square kilometers.
If there were 100 cells in this raster, each cell would represent one square kilometer of equal width and height (that is, 1 km x 1 km).

## Slide 28: Resolution and Cell Size
Notes: The dimension of the cells can be as large or as small as needed to represent the surface conveyed by the raster dataset and the features within the surface, such as a square kilometer, square foot, or even a square centimeter.
The cell size determines how coarse or fine the patterns or features in the raster will appear. The smaller the cell size, the smoother or more detailed the raster will be.
However, the greater the number of cells, the longer it will take to process and it will increase the demand for storage space. If a cell size is too large, information may be lost or subtle patterns may be obscured.

## Slide 29: Resolution and Cell Size
Grid Cell Width = 30 feet
Grid Cell Width = 300 feet

## Slide 30: Cell size
Choose raster cell size 1/2 the length (1/4 the area) of smallest feature to map (smallest feature called minimum mapping unit or resel--resolution element)
A raster dataset can always be re-sampled to have a larger cell size; however, you will not obtain any greater detail by re-sampling your raster to have a smaller cell size.
Depending on your future plans for your data, it may be worthwhile to store a copy of your data at its smallest and most accurate cell size, meanwhile re-sampling it to match that of your least—this could increase your analysis processing speed.

## Slide 31: Cell Location
The location of each cell is defined by the row or column where it is located within the raster matrix.
Essentially, the matrix is represented by a Cartesian coordinate system, in which the rows of the matrix are parallel to the x-axis and the columns to the y-axis of the Cartesian plane.
Row and column values begin with 0.

## Slide 32: Raster Data Formats
GRID is ESRI’s proprietary format for storing and processing raster data
Standard industry formats for image data such as JPEG, TIFF and MrSid formats can be used to display raster data, but not for analysis (must convert to GRID)
Georeferencing information required to display images with mapped vector data
  Requires an accompanying “world” file which provides locational information

## Slide 33: Why store data as a raster?
Sometimes you don't have the choice whether to store your data as a vector or raster; for example, imagery is only available as a raster.
The advantages of storing your data as a raster are:
  A simple data structure: A matrix of cells with values representing a coordinate and sometimes linked to an attribute table
  A powerful format for advanced spatial and statistical analysis
  The ability to represent dense, continuous surfaces and to perform surface analysis
  The ability to uniformly store points, lines, polygons, and surfaces
  The ability to perform fast overlays with complex datasets
Notes: Show Figure 4.35 from textbook here

## Slide 34: Other considerations
There are other considerations that may convince you to use a vector-based storage option. For example:
  There can be spatial inaccuracies due to the limits imposed by the raster dataset cell dimensions.
  Raster datasets are potentially very large datasets. Resolution increases as the size of the cell decreases; however, normally cost also increases in both disk space and processing speeds. For a given area, changing cells to one-half the current size requires as much as four times the storage space, depending on the type of data and storage techniques used.

## Slide 35: Raster vs. Vector
Raster is faster, but raster is vaster, and vector just seems corrector.
Paraphrased from C. Dana Tomlin