## Slide 1: Open educational resources for introduction to geographic information systems funded by: USG affordable learning grant
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Department of Geography and Anthropology
Module 5
Geocoding

## Slide 2
Module Overview
Geocoding

## Slide 3
Geocoding – refers to the process of assigning spatial locations to data that are in tabular format but have fields that describe their locations.
Address matching – the most common type of geocoding is address geocoding or address matching, which plots street addresses as point features on a map.
Address matching requires two sets of data:
The first data set contains individual street addresses in a table, one record per address.
The second is a reference database that consists of a street map and attributes for each street segment such as the street name, address ranges, and ZIP codes.
Address matching interpolates the location of a street address by comparing it with data in the reference database.
WHAT IS GEOCODING?

## Slide 4
Examples of geocoding applications
  A police department could use address geocoding to analyze crimes by address. These locations can be mapped and analyzed with other demographic data.
  Emergency dispatch operators could use geocoding to enter an address, determine who should respond, and route emergency vehicles and personnel to the address.
  A school district could use geocoding to match student addresses against a street map of the city. Once the homes of the students are located, school assignments and busing plans can be created and analyzed.
Geocoding examples

## Slide 5
Mechanism of geocoding:
  The process is based on a comparison of each address in the address table against the address ranges by street of the reference theme.
  When an address is matched against a particular address range of the reference theme, the system performs an interpolation to locate and assign real world coordinates to the address.
  It is an estimation of where the address is located.
How does it work?

## Slide 6
Prepare Address Data
Select Reference Data
Define Matching Strategies (style)
Standardization
Blocking
Create Index
Matching
Review/Edit
Automated in ArcGIS
Process of geocoding

## Slide 7
Address Number
Street Prefix
Street Name
Street Suffix
Street Type
City
State
Zip Code
County
Country
Descriptive Elements of an Address

## Slide 8
Incorrect address information
Minimal format verification
Spelling errors
  Appalachian
  Appalayshun
  Apalitean
  Apalachian
Irregular Addresses
One Twenty Three Smith St.
US Hwy 281
PO Box 234
RR 18 Box 131
Potential errors in addresses

## Slide 9
To give you an idea of the matching process, try finding the address range in Column B that matches each address in Column A.
The first and second numbers of the addresses listed in Column B are the house number range on the left side of the street, while the third and fourth numbers are the house number range on the right side of the street.
Column A | Column B
a) 620 Center Street | 1) 501 599 500 598 Center Av
b) 710 Palm Av W | 2) 601 699 600 698 Center St
c) 680 1st Street | 3) 701 799 700 798 Palm Av W
 | 4) 701 799 700 798 Palm Av E
 | 5) 651 699 650 698 First St
How does the matching work?

## Slide 10
Column A | Column B
a) 620 Center Street | 1) 501 599 500 598 Center Av
b) 710 Palm Av W | 2) 601 699 600 698 Center St
c) 680 1st Street | 3) 701 799 700 798 Palm Av W
 | 4) 701 799 700 798 Palm Av E
 | 5) 651 699 650 698 First St
620 Center Street matches number 2 in Column B because the street name is the same and the address range, 600 to 698, matches. The street type, Street, matches the abbreviated form of St.
When two features have the same street name, type and range of numbers, such as in the second example, the direction becomes critical to decide which feature matches.
Matching continued

## Slide 11
An Interpolation – An estimation of where a particular address is located on your reference theme.
The address you would like to geocode is 6 N Main Street.
Your reference theme has a segment on Main Street where the address range is 2 to 10 N Main street, so the location would be estimated to fall in the middle of that line.
What is an interpolation?

## Slide 12
Address matching is a laborious process and is a function of the accuracy of the address table and reference theme.
Usually, the address table will have typos, incorrectly spelled street names, blanks, common names, etc.
Make sure and be prepared to have a verification process. i.e. a good atlas
Caution, warnings