## Slide 1: Open educational resources for introduction to geographic information systems funded by: USG affordable learning grant
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Department of Geography and Anthropology
Module 6
Geoprocessing

## Slide 2: Overview
Basic Geospatial Analysis Techniques
Spatial Selections
What is a Buffer?
Dissolve Operation
Overlay Operations Vector Overlay
Basic Cases of Overlay - Clip
Basic Cases of Overlay - Intersection
Basic Cases of Overlay - Union
Vector Overlay Problems

## Slide 3: Summary
Geospatial data analysis is the application of operations to manipulate or calculate coordinates and/or related attribute data.
Geospatial data analysis is applied to solve problems such as bus routes, determining flood zones, and in determining suitable sites for construction.
Spatial data analysis uses spatial operations to manipulate or calculate. This is in contrast to analysis that does not use spatial operations to manipulate or calculate.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 4: Spatial selections
Spatial Selections
  Adjacency
  Containment
  Distance
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 5: buffer
A buffer is a region that is less than or equal to a distance from one or more input features.
Buffers can be created from point/line/polygon/raster geospatial data sets.
Buffers are typically used to identify areas or objects “inside”, or “outside” the threshold distance.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 6: dissolve
The dissolve operation combines similar features within a data layer based on a shared attribute.
The dissolve field can have as many different values as you choose; however, only records with identical values for that attribute will be combined into a single feature.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 7: Overlay operations
Overlay operations involve combining spatial and attribute data from two or more spatial data layers. In other words, we are stacking the data, and looking for where the layers overlap.
One thing to note about overlay operations is that overlays require that the data be in the same coordinate system.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.

## Slide 8: Vector Overlay
A vector overlay involves combining point, line, or polygon geometry and their associated attributes. All overlay operations create new geometry and a new output geospatial data set.
Examples of vector overlay tools are clip, intersect and union.
Notes: A lake is a discrete object within the surrounding landscape. Where the water’s edge meets the land can be definitively established. Other examples of discrete objects include buildings, roads, and parcels.