## Slide 1: OPEN EDUCATIONAL RESOURCES FOR INTRODUCTION TO GEOGRAPHIC INFORMATION SYSTEMS FUNDED BY: USG AFFORDABLE LEARNING GRANT
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Module 7
Digitizing and Editing
Department of Geography and Anthropology

## Slide 2: Data Encoding
Data encoding – Process of getting data
into computer
GIS without data will not produce
output
Data can be obtained from many
different sources
There are also many different methods
of data encoding possible
Notes: 2

## Slide 3: Data Editing
Once geospatial data is in GIS, corrections and manipulations can be made
Data editing- Process of reviewing and correcting collected data

## Slide 4: Data Stream
Data stream = The processes of data encoding and data editing
Analogue data (non-digital) must be made digital (computerized) first to be used in a GIS
Data encoding and integration can be lengthy due to different type, format, scale and resolution
Notes: 4

## Slide 5: Data Stream:
Data Sources
Data Capture
Data Editing
Final Integrated GIS Database

## Slide 6: Data Sources
Map (scanned, digital, analogue map)
Aerial photo and satellite images
GPS/GNNS
Digital data via internet.
Tabular data

## Slide 7: Obtaining Data from other sources
What data are available?
What will the data cost?
How will the data be supplied? How long will it take to get it?
What format will the data be in?

## Slide 8: Data Capture
Digitizing
Using a computer and mouse to trace features and digitize them manually
Scanning
Automatic digitizing, using scanner to create digital raster file of lines (automatic line follower)
Electronic Data transfer
Data collected digitally from GPS receivers, total stations, data loggers, handheld devices or via internet.
Often reformatting (data conversion) necessary Keyboard entry/keycoding
For small data sets and attributes- Tabular data

## Slide 9: Possible encoding methods for different data sources
Data Source | Analogue or digital source | Encoding method | Example
Tabular data | Analogue | Keycoding, text scanning | Address lists of hotel guests
Map data | Analogue | Manual digitizing, automatic digitizing, scanning | Historical maps
Map data | Digital | Digital file transfer | DTM, Digital topographic data
Field survey | Analogue | Keycoding | National population census data
Field Survey | Digital | Digital file transfer | Data from meteorological station recording equipment
Aerial photos | Analogue | Manual digitizing, automatic digitizing, scanning | Ski slope locations
Aerial photos | Digital | Digital file transfer | Ski slope locations
GPS/GNSS | Digital | Digital file transfer | 
Satellite imagery | Digital | Digital file transfer, image processing | Forest condition data

## Slide 10: Heads up Digitizing
“Interactive, or heads-up digitization, is one of the most common methods. In this method, you display an aerial photograph, satellite image, or orthophotograph on-screen as a basemap, then you draw features, such as roads, buildings, or parcels, on top of it.”
http://desktop.arcgis.com/en/arcmap/10.3/manage-data/editing/what-is-editing-.htm

## Slide 11: Data Editing:
Editing and cleaning
Re-Projection and Scale
Generalization
Edge Matching and rubber sheeting
Layering

## Slide 12: Editing
Editing occurs in an edit session.
During an edit session, you can create or modify vector features or tabular attribute information.
http://desktop.arcgis.com/en/arcmap/10.3/manage-data/editing/what-is-editing-.htm

## Slide 13: Editing
http://desktop.arcgis.com/en/arcmap/10.3/manage-data/editing/what-is-editing-.htm

## Slide 14: Editing Existing Features
http://desktop.arcgis.com/en/arcmap/10.3/manage-data/editing/what-is-editing-.htm

## Slide 15: Data Editing
Check for errors
  Errors in source data
  Errors from encoding process
  Errors propagated during transfer and conversion
Compare with source data
Common digitizing errors

## Slide 16: Common digitizing errors in vector data
Unclosed polygon
Overshoot
Duplicate line segment
Duplicate label points
Unlabeled polygon
Spike
Loop or knot
Dangling node
Pseudonode

## Slide 17
Examples of original data problems and the corrected data after processing
Source: Laser-Scan. Copyright © 2005 LS 2003 Ltd. All rights reserved

## Slide 18: Data Editing ( cont.)
Re-projection may be necessary to overlay data spatially
Common coordinate system must be used which may require transformation
Scale is only as good as the worst (smallest scale) used – other data generalized to decrease unnecessary detail and file size

## Slide 19
Topological mismatch between data in different projections
Source: Courtesy of Peter H. Dana

## Slide 20
The results of repeated line thinning
Sources: (a–f): From The Digital Chart of the World. Courtesy of ESRI. Copyright © ESRI. All rights reserved; (inset): From ESRI, ArcGIS online help system, courtesy of ESRI. Copyright © 2005 ESRI. All rights reserved

## Slide 21
Edge matching
When a study area extends across two or more map sheets, each map sheets would be digitized separately and then the adjacent sheets join after editing, re-projection, and generalization. Small differences or mismatches between adjacent map sheets will be resolved through this joining processes called edge matching

## Slide 22: Editing databases
Attributes of databases must be maintained and updated to be useful
In a geodatabase, the existing length and area attributes become updated automatically, but other attributes will need to be updated manually.
  Can edit values one-at-a-time in attribute table
  Can use Field Calculator to assign values to entire field