## Slide 1: OPEN EDUCATIONAL RESOURCES FOR INTRODUCTION TO GEOGRAPHIC INFORMATION SYSTEMS FUNDED BY: USG AFFORDABLE LEARNING GRANT
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Module 9
Global Navigation Satellite Systems (GNSS)
Global positioning Systems (GPS)
Department of Geography and Anthropology

## Slide 2
Global Navigation Satellite Systems (GNSS)
  USA = GPS (Global Positioning System)
  Russia = GLONASS
  European Union = Galileo
  China = BeiDou

## Slide 3
http://stuffin.space

## Slide 4: History of GPS
Began in 1973
Owned and operated by the US government
Maintained by the Dept. of Defense
Non-degraded civilian use required by law since 1990s

## Slide 5: History of GPS
First satellite launched in 1978 – Navstar 1
Fully operational 1995
Satellites orbit Earth every 12 hours
Altitude – app. 20,200 km or 12,600 miles

## Slide 6: GPS Uses
Vehicle Navigation
Hiking
Aids for Visually Impaired
Disaster Relief
Autonomous Vehicles
Cartography
Cellular Telephony
Clock Synchronization
Geofencing: Tracking
Geotagging
Mining
Robotics
Sports
Surveying
Tectonics
Military Applications

## Slide 7: How GPS Works
3 Main components:
  • User Segment: owned receivers
  • Space Segment: Satellites
  • Control Segment: Ground control and monitoring stations

## Slide 8: How GPS Works
  Accurate Timing
  Satellite Positioning
  Satellite Distance Ranging
  Trilateration
  Error Correction
https://www.youtube.com/watch?v=4O3ZVHVFhes

## Slide 9: How GPS Works 3d
http://www.trimble.com/gps/howgps-triangulating.shtml
24+ operational satellites located in 6 orbital planes.
To determine position, signals from at least 4 satellites are needed if no other information is available

## Slide 10: How GPS Works
Accurate Timing
  Ensures accurate calculation of distance
  Atomic clocks on each satellite are accurate to the nanosecond (one billionth of a second)
  0.000000001 second (1.0 x 10 -9 sec)
    -use the resonance frequencies of atoms
    -e.g. an atom of cesium resonates at an exact frequency

## Slide 11: How GPS Works
Satellite Positioning
  The satellites must know where they themselves are
  Radar from ground station constantly checks each satellite to monitor changes in orbit

## Slide 12: How GPS Works
Satellite Ranging
  Measuring the distance from the satellites to receiver
  D = ST
    D is Distance between satellite and receiver
    S is Speed of signal: 299 792 458 m / s (in vacuum)
    T is Time it takes for signal to be sent and received

## Slide 13: GPS accuracy
Under ideal conditions ~3 meters
Error can increase to ~10 meters
Sources of error:
  Atmospheric interference
  Multipath error (interference from ground or man-made structures)
  Clock Timing
  Number of Satellites in View
  Satellite Geometry
  Behavior of Signal Under Canopy

## Slide 14: Issues of Precision
Clock Timing
  Clocks running fast or slow can effect distance calculation
  Controlled by ground stations
  Einstein to thank for this – Special Relativity
    Clocks will tick at different speeds due to gravitational changes

## Slide 15: Issues of Precision
Atmospheric Effects
  Assumption is speed of light in vacuum
  Reality: travels through gases in atmosphere
    More atmosphere, more delay
http://www.trimble.com/gps/howgps-error.shtml

## Slide 16: Issues of Precision
Atmospheric
“Elevation Mask”

## Slide 17: Issues of Precision
Error under certain geometric situations
Good Range Fix
Poor Range Fix

## Slide 18: Issues of Precision
Multipath
  Correct for by using quality antennas that block signals from incorrect angles

## Slide 19: Wide Area Augmented System (WAAS)
  Ground Stations in US
  Calculate differential info and beam to satellite
Designed to provide real-time
accuracies within 7 meters or less
  Geosynchronous Satellite sends info down to receivers

## Slide 20: Smartphone VS. GPS Units
Low end GPS receivers have been replaced with smart devices
Smartphone technology has a consumer grade GPS receiver
Assisted Global Positioning System (AGPS) used by your smartphone pings cell towers for triangulation to geolocate. There should be at least 3+ cell towers visible from your phone for your phone company to be able to locate where you are. The accuracy will depend on the strength between your phone and cell tower.
Professional grade precision GPS units have a much higher degree of accuracy
-smart phones currently cannot replace professional GPS