## Slide 1: OPEN EDUCATIONAL RESOURCES FOR INTRODUCTION TO GEOGRAPHIC INFORMATION SYSTEMS FUNDED BY: USG AFFORDABLE LEARNING GRANT
Created by:
Ulrike Ingram
Allison J. Bailey
Amber Ignatius
Katayoun Mobasher
Mark Patterson
Module 10
Coordinate Systems & Projections
Department of Geography and Anthropology

## Slide 2: Coordinate Systems & Projections
Introduction to
Geographic Information Science (GIS)

## Slide 3
The University follows the section 508 Standards and WCAG 2.0 for web accessibility. If you require any content from this module in another format, please send an email to your instructor.

## Slide 4: Earth’s shape: oblate spheroid
imperfect sphere due to rotational axis
-bulges at the equator, flattens at the poles
https://www.quora.com
Note: this is exaggerated!

## Slide 5: Datum
Datum: defines surface of the earth and position of that surface (usually relative to earth’s center)
Common Datums ...
• North American Datum NAD27, NAD83
• World Geodetic System WGS84
New Datum coming in 2022!
Note Exaggerated Scale! Source: ESRI Geodesy
Notes: Image credit: https://www.arcgis.com/apps/Cascade/index.html?appid=62fede405d3141c48a4f170f2ce27556

## Slide 6
https://www.ngs.noaa.gov/corbin/class_description/NGS_Datums_video_2c/

## Slide 7: How to describe location?
Where am I?!

## Slide 8: Coordinate systems
A coordinate system is a framework that uses points, lines, and surfaces to determine location in 2 or 3 – dimensional space

## Slide 9: Geographic Coordinate systems
Geographic Coordinate System (GCS):
  3D coordinate system.
  Measurement using angles anchored at Earth’s center.
Latitude:
Measures north or south of equator
Longitude:
measures east or west of Prime meridian
McKnight

## Slide 11
30°N,
50°W

## Slide 12: Latitude and longitude
Measure angles, not distances
Expressed in terms of…
  degrees minutes seconds (DMS) (40° 26′ 2″ N latitude)
  decimal degrees (DD) (40.434°)

## Slide 13: Map projections
Projected coordinate systems: Change 3D Geographic Coordinate System (lat/long) to… 2D flat Cartesian system (meters, feet)

## Slide 14: Common map projections
Conic
Cylindrical
Planar
GIS TUTORIAL 1 - Basic Workbook. ESRI

## Slide 15: Cylindrical projection
Parallels and meridians at right angles
Size/shape/area of large objects distorted (scale approaches infinity at the poles!)
  Example: Mercator projection (1569)
  used for nautical purposes (constant courses are straight lines)
GIS TUTORIAL 1 - Basic Workbook. ESRI

## Slide 16: Conic projection
Preserves accurate area
Scale and shape are not preserved
  Example: Albers Equal Area
  standard projection for US Geological Survey, US Census Bureau
GIS TUTORIAL 1 - Basic Workbook. ESRI

## Slide 17: Compromise projections
Neither equivalent nor conformal
Meridians curve gently, avoiding extremes.
Doesn’t preserve properties, but “looks right”
  Example: Robinson projection (1961)
  good compromise projection for viewing entire world
  used by Rand McNally and National Geographic Society
GIS TUTORIAL 1 - Basic Workbook. ESRI

## Slide 18: Map projections
Power and Limits of Maps

## Slide 19: Universal Transverse Mercator (UTM)
UTM Projected Coordinate System divides Earth into 60 vertical zones that are 6° longitude wide, avoids poles.
  • coordinates measured in meters
  Common!

## Slide 20: State Plane Coordinate System
https://geodesy.noaa.gov/SPCS/
SPCS uses different local projections for 126 zones of the U.S.
  • east-west zones use Lambert Conformal Conic (conic)
  • north-south zones use Transverse Mercator (cylindrical)
  • coordinates measured in feet
  Common!

## Slide 21
Based on model of Earth’s shape called a “datum” (ex: NAD83, WGS84)
Location described using angles (latitude and longitude)
Geographic Coordinate Systems
(3D)
Projected Coordinate Systems (2D)
Based on a datum and GCS and then converted to a flat map
Ex: Transverse Mercator, Lambert Conformal Conic
Location described using linear units of measurement (e.g. m, ft)
https://communityhub.esriuk.com/geoxchange/2012/3/26/coordinate-systems-and-projections-for-beginners.html
  Review!

## Slide 22: Map projections
Remember: all maps are distorted in shape, area, or distance
  Review!

## Slide 23: Map projections
https://www.youtube.com/watch?v=kIID5FDi2JQ

## Slide 24: Bonus review…
https://www.youtube.com/watch?v=Z41Dt7_R180
Detailed explanation of datum and projections

## Slide 25: Bonus review…
Geographic coordinate systems (lat/long) are based on a spheroidal (either truly spherical or ellipsoidal) surface that approximates the surface of the earth.
A datum typically defines the surface (e.g. radius for a sphere, major axis and minor axis or inverse flattening for an ellipsoid) and the position of the surface relative to the center of the earth. An example of a datum is NAD84
A projection is a series of transformations which convert the location of points on a curved surface (the datum reference surface) to locations on a flat plane.
From: https://gis.stackexchange.com/questions/664/whats-the-difference-between-a-projection-and-a-datum/1328