## Slide 1: Internet and Networking Basics

## Slide 2: Learning outcomes
After completing this lesson, you will be able to:
  Describe the nuts and bolts view of the Internet
  Define IP address and explain its role in the Internet
  Demonstrate how information travels in a packet-switched network
  Demonstrate the role of network layers and protocols
  Explain the unique characteristics of the Internet
  Explain why the architecture of the Internet is inherently insecure

## Slide 3: The “nuts and bolts” View
millions of connected computing devices:
  hosts = end systems
  Connected by
    routers and switches
communication links
  fiber, copper, radio, satellite

## Slide 4: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
  IXP: Internet eXchange Point
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 5: How a System/Device is Identified on the Internet: IP Addresses
Each computer connected to the Internet must have a unique address: IP (Internet Protocol) address
Internet addresses are in the form nnn.nnn.nnn.nnn where nnn must be a number from 0 - 255. This address is known as an IPv4 address.

## Slide 6: How many possible IP addresses are There?
256 x 256 x 256 x 256 = 4,294, 967,296
How many devices are connected to the Internet ?
More than 4.3 billion! 127 items per second according to an article at the NetworkWorld:
  http://www.networkworld.com/article/2942596/microsoft-subnet/127-devices-added-to-the-internet-each-second-but-congress-is-clueless-about-iot.html
  So IPv4 addressing scheme is not enough. IPv6 is the new scheme!

## Slide 7: IPv6
The next generation Internet Protocol (IP) standard intended to eventually replace IPv4.
IPv6 address has 128 bits:
Example: DE10:2D7B:0000:0CDE:1257:0000:211E:729C
(32 hexadecimal digits)
The number of potential IPv6 addresses has been calculated as:
340,282,366,920,938,463,463,374,607,431,768,211,456

## Slide 8: Domain Names

## Slide 9: DNS: Domain Name System
Mapping of (user-friendly) URL to IP address:
URL
IP Address
The Internet: IP Addresses and DNS by code.org

## Slide 10: What is your IP?
To find your IP you can do one of these:
http://whatsmyip.net/
OR
Click the START icon at the bottom left corner
  Type cmd in the text box
  When the window for command prompt appears, type ipconfig

## Slide 11: Networking and Protocols

## Slide 12: How files travel from one machine to another
Each file is broken into small packets
Each packet is like an envelope with content inside
Each packet contains source and destination addresses
Each packet travels through the Internet and goes from one machine to another via several routers

## Slide 13: The original design goals of the Internet
It should be open, neutral and simple network
It should be completely independent of software or hardware platforms
It should be scalable
It should be suitable to new applications and new hardware/software

## Slide 14: The main features of the Internet
Open
Scalable
Asynchronous
Supported new innovations and application and led to the enormous growth
Supported variety of devices in huge numbers
Supported communication speed and many-to-many interaction

## Slide 15: Discussion
List some of the vulnerabilities that are created by the main features of the Internet.

## Slide 16: How packets travel
Watch this video on how packets travel from code.org:
The Internet: Packets, Routing and Reliability

## Slide 17: Check It Out - The Ping Program
Ping is a software utility used to test the reachability of a host on an Internet Protocol (IP) network and to measure the round-trip time for messages sent from the originating host to a destination computer and back.
Click the START icon at the bottom left corner
Type cmd in the text box
When the window for command prompt appears, type
ping www.columbusstate.edu
Observe what happens

## Slide 18: Traceroute
Traceroute is a command which can show you the path a packet of information takes from your computer to one you specify. It will list all the routers it passes through until it reaches its destination, or fails to and is discarded. In addition to this, it will tell you how long each 'hop' from router to router takes.
In Windows, start the cmd prompt. Enter the word tracert, followed by a space, then the domain name.
Firstly it tells you that it's tracing the route to the destination, the IP address of that domain, and what the maximum number of hops will be before it times out.
Next it gives information about each router it passes through on the way to its destination.

## Slide 20: OSI Model
The Open System Interconnection (OSI) model defines a networking framework to implement protocols in seven layers. Control is passed from one layer to the next, starting at the application layer in one station, and proceeding to the bottom layer, over the channel to the next station and back up the hierarchy. http://www.webopedia.com/quick_ref/OSI_Layers.asp

## Slide 21: 7 Layers of the OSI Model

## Slide 22: OSI Layers at Work

## Slide 23: OSI Model and Protocols

## Slide 24: OSI Layers and Headers
Note that at each layer some header information is added to the data to let the other side know how to handle the packet.

## Slide 25: Internet travel explained by OSI model
Application layer
Application layer
Transport layer
Transport layer
Network layer
Network layer
Physical layer
Physical layer
Data is prepared
Packets are created, headers added
IP headers added
More headers added
Packets go to the next device
Network layer
Physical layer
Physical layer header is read
Network layer header is read
Transport layer header is read, packets are reassembled
The file is delivered to the appropriate application
Physical layer header is read
Network layer header is read
Physical layer header is modified
Network layer header is modified

## Slide 26: Discussion question
What is the importance of layered OSI model ?
  Who benefits from the OSI model?
  How?

## Slide 27: Wireshark
Wireshark is a free and open source packet capture tool and analyzer used for network troubleshooting, analysis, software and communications protocol development, and education.
You can download and read about wireshark at
https://www.wireshark.org/
In some of your Netlab assignments you will make use of wireshark to complete certain steps in the lab.

## Slide 28: TCP: Transport Layer Protocol
Reliable:
  Data is guaranteed to arrive, and in the correct order without duplications
  Or the connection will be dropped
Full-duplex, connection-oriented:
  Communicating systems must establish a connection between them before exchanging packets

## Slide 29: Ports
A number that identifies a channel in which communication can occur
65,635 possible ports
Knowing what port a packet was destined for (or coming from) tells you what protocol it was using

## Slide 30: Ports (cont.)
Type of Port | Port Numbers
Well-known ports | 0 to 1023
Registered ports | 1024 to 49151
Dynamic ports | 49152 to 65535

## Slide 31: Some Important Ports
Port Number | Protocol that Uses Port
20, 21 | File Transfer Protocol (FTP)
22 | Secure Shell (SSH)
23 | Telnet
25 | Simple Mail Transfer Protocol (SMTP)
53 | Domain Name System (DNS)
80 | Hypertext Markup Language (HTML)
110 | Post Office Protocol Version 3 (POP3)
Notes: Consider the information you gather from these ports.
Assume you capture traffic going to and from a database server on port 21. This means someone is using FTP to upload or download files with that server. But you
query the network administrator and find he or she doesn’t use FTP on his or her database server. This is likely a sign of an intruder or, at the very least, of an insider who is not adhering to system policy.
Frequent attempts to connect to a Web server on port 23 (Telnet) is evidence of a well-known old hacker trick, which is to attempt to telnet into a Web server and grab the server’s banner or banners. This allows the hacker to determine the exact operating system and Web server running unless the system administrator has modified the banner to avoid this hacker trick.

## Slide 32: TCP Segment
Destination Port
Acknowledgment Number
Options...
Padding
Data...
0
4
10
16
19
24
31
Source Port
Window
Len
Sequence Number
Reserved
Flags
Urgent Pointer
Checksum
Field Purpose
Source Port Identifies originating application
Destination Port Identifies destination application
Sequence Number Sequence number of first octet in the segment
Acknowledgment # Sequence number of the next expected octet (if ACK flag set)
Len Length of TCP header in 4 octet units
Flags TCP flags: SYN, FIN, RST, PSH, ACK, URG
Window Number of octets from ACK that sender will accept
Checksum Checksum of IP pseudo-header + TCP header + data
Urgent Pointer Pointer to end of “urgent data”
Options Special TCP options such as MSS and Window Scale
Notes: 27

## Slide 33: TCP Three-Way Handshake
Synchronize (SYN)
Acknowledge (ACK)
1. SYN
2. SYN/ACK
3. ACK
Connection established
Listening to client until the connection lasts
Communicating to server as long as it lasts
Notes: The TCP three-way handshake used by TCP establishes a session between two systems.
The first system sends a packet with the SYN flag set.
The second system responds with a packet that has the SYN and ACK flags set.
The first system responds with a packet with the ACK flag set.
The two systems have now started a session.

## Slide 34: TCP Connection Termination
1. ACK/FIN
2. ACK
4. ACK
Connection terminated
No more listening to the client
No more communication with server
3. ACK/FIN
Acknowledge (ACK)
Finish (FIN)
Notes: Because a TCP connection is two-way, it needs to be “torn down” in both directions.
The TCP connection termination process uses four packets.
The first system sends a TCP packet with the ACK and FIN flags set requesting termination.
The second system sends an ACK response.
The second system then sends a packet with ACK and FIN flags set.
The first system returns an ACK response.

## Slide 35: TCP Connection Reset
Server
Host
1 – SYN
2 – SYN/ACK
3 – RST
Synchronize (SYN)
Acknowledge (ACK)
Reset (RST)
Notes: Sometimes a host may need to terminate a connection quickly, due to a port being unreachable or a timeout, for example.
Can send a Reset (RST) packet.
Initial SYN packet should never have FIN or RST associated with it. Indicates an attack/malicious attempt to get by your firewall.

## Slide 36: Question
What happens if the client machine does not send the ACK packet to the server in the 3rd step of 3 way handshake ? How do the server respond?

## Slide 37: TCP : Data transfer
Receiver
Sender
Packet Lost
Timer
Timer
Pkt 0
ACK 0
Pkt 1
ACK 1
Pkt 3
ACK 3
Pkt 2
ACK 2
Receiver
Sender
Pkt 0
ACK 0
Pkt 1
ACK 1
Pkt 1
timeout
Receiver
Sender
Pkt 0
ACK 0
Pkt 1
Pkt 1
timeout
ACK 1
Duplicate packet is deleted

## Slide 38: Packets from Wireshark

## Slide 40: IP Routing: Network Layer
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Source
Destination
Router

## Slide 41: IP Datagram
Vers
Len
TOS
Total Length
Identification
Flags
Fragment Offset
TTL
Protocol
Header Checksum
Source Internet Address
Destination Internet Address
Options...
Padding
Data...
0
4
8
16
19
24
31
Field Purpose
Vers IP version number
Len Length of IP header (4 octet units)
TOS Type of Service
T. Length Length of entire datagram (octets)
Ident. IP datagram ID (for frag/reassembly)
Flags Don’t/More fragments
Frag Off Fragment Offset
Field Purpose
TTL Time To Live - Max # of hops
Protocol Higher level protocol (1=ICMP,
6=TCP, 17=UDP)
Checksum Checksum for the IP header
Source IA Originator’s Internet Address
Dest. IA Final Destination Internet Address
Options Source route, time stamp, etc.
Data... Higher level protocol data
We only looked at the IP addresses, TTL and protocol #
Notes: 16

## Slide 42: Routing
How does a device know where to send a packet?
  All devices need to know what IP addresses are on directly attached networks
  If the destination is on a local network, send it directly there

## Slide 43: Routing
If the destination address isn’t local
  Most non-router devices just send everything to a single local router
  Routers need to know which network corresponds to each possible IP address

## Slide 44: Routing Table
Source: https://technet.microsoft.com/en-us/library/cc787509(v=ws.10).aspx

## Slide 45: Link Layer :
Terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
Link layer has responsibility of transferring datagram from one node to adjacent node over a link.

## Slide 46: Link Layer Addressing
32-bit IP address:
  network-layer address
  used to get packet to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get packet from one interface to another physically-connected interface (same network)
  48 bit MAC address
    burned in NIC ROM, also sometimes software settable
    unique for each adapter

## Slide 47: Quiz
Which layers are present at every router?
  Application, transport, network, physical
  Transport, network, physical
  Network, physical
  Physical

## Slide 48: Question
Why do routers not have application and transport layer?