## Slide 1: Network Security

## Slide 2: What ways do you see of getting in?
The Internet
De-Militarized
Zone
Private Network
Border Router
Commercial Network
Private Network
WLAN
Notes: What is the easiest way to get into this network? It may not be through the firewalls. It may be through the dial-up access, CDs or DVD drives, or WLANs.
Also notice that a good network will be divided into sections. The De-Militarized Zone here is for public access. The Private Network is for internal access, and requires going through 2 firewalls, each with filtering.

## Slide 3: Attacking the Network
The Internet
De-Militarized
Zone
Private Network
Border Router/
Firewall
Router/Firewall
WLAN
Notes: The Path of Logical Access shows where requests enter and are processed.
Two paths of logical access are shown, via brown arrows through WLAN and to server, and red arrows through laptop and server.
Visitors from the internet must get through a firewall, then either the logical access controls (LAC) in the database servers in the demilitarized zone (DMZ), or through a second firewall and the LAC in the internal network’s servers. Entering via the wireless LAN bypasses all that (except for the internal LAC), as does using a disk or flash drive. The latter (wireless/portable media access) shows that this organization depends on physical controls and internal access control mechanisms (including employee trustworthiness) to prevent unauthorized use by those means. This leaves the private network server and the printer vulnerable.

## Slide 4: The Challenge of Network Security
The Internet allows an attacker to attack from anywhere in the world from their home desk.
An attacker needs to find just one vulnerability; a security analyst need to close every vulnerability.

## Slide 5: Defense in Depth
Manage risk with diverse defensive strategies
Avoid single point of failure

## Slide 6: NETWORK DEFENSE MECHANISMS
Firewalls
DMZ
IDS/IPS
VPN
Honeypots/Honeynets
Logs
Redundancy Systems
Backup
Access Control

## Slide 7: Firewalls
Packet Filtering:
  Packet header is inspected
  Single packet attacks caught
  Very little overhead in firewall: very quick
  High volume filter
Stateful packet inspection
  More fields in packet header inspected
  State retained in firewall memory
  Most multi-packet attacks caught
  Little overhead in firewall: quick

## Slide 8: Firewalls Continued
Deep Packet Inspection
  Actual content analyzed
  Content reassembled to check what is delivered to the application
  All multi-packet attacks caught
  High overhead in firewall: slow
Proxy Servers
  Packet session terminated and recreated via a Proxy Server
  Packets disassembled an
  Most or all of application inspected
  Highest overhead: slow & low volume

## Slide 9: DMZ –Demilitarized Zone
A physical or logical subnetwork that contains and exposes an organization's external-facing services to a larger and untrusted network (Internet)
Adds an additional layer of security to the local area network (LAN)
An external network node has direct access only to the equipment/services in DMZ (web, email, dns)
Neither as secure as the internal network, nor as insecure as the public internet
Hosts in the DMZ are permitted to have only limited connectivity to specific hosts in the internal net
A DMZ configuration provides security from external attacks, but it typically has no bearing on internal attacks such as sniffing communication or spoofing an email address

## Slide 10: IDS/IPS Intrusion Detection/Prevention Systems
IDS: A device or software application that monitors network or system activities for malicious activities or policy violations and produces alarms/electronic reports to a management station
IPS: Acts on alarms
Two types of IDSes based on where they are placed:
Network IDS (NIDS): At a strategic point or points within the network to monitor traffic to and from all devices on the network.
Host IDS (HIDS): On individual hosts or devices on the network; monitors the inbound and outbound packets from the device only

## Slide 11: IDS - Based on the Technique Used for DETECTION
Signature-based
  Monitors packets on the network and compare them against a database of signatures of attributes from known malicious threats
Anomaly-based
  Monitors network traffic and compare it against an established baseline

## Slide 12: Honeypot & Honeynet
Honeypot: A system with a special software application which appears easy to break into
Honeynet: A network which appears easy to break into
Purpose: Catch attackers
All traffic going to honeypot/net is suspicious
If successfully penetrated, can launch further attacks
Must be carefully monitored
External DNS
IDS
Web Server
E-Commerce
VPN
Server
Firewall
Honey
Pot
Notes: A Honeypot or Honeynet has no useful purpose other than to catch attackers. It may be used as a form of an IDS. While it sounds fun and interesting, they need to be maintained and monitored: if an attacker does gain entry, they now can attack from within the network.

## Slide 13: Remote Access Security: VPN
Virtual Private Network (VPN) often implemented with IPSec
Can authenticate and encrypt data through Internet (red line)
Easy to use and inexpensive
Difficult to troubleshoot, less reliable than dedicated lines
Susceptible to malicious software and unauthorized actions
Often router or firewall is the VPN endpoint
The Internet
Firewall
VPN
Concentrator
Notes: A VPN creates an encrypted point-to-point path between two computers. Here the line in red is encrypted.
Often it uses Public Key Encryption to communicate a Secret Key, then uses Secret Key encryption to encrypt the session data.

## Slide 14: IPSec: Tunnel and Transport Modes
original IP headers remain intact
http://www.firewall.cx/networking-topics/protocols/870-ipsec-modes.html
whole packet including the IP address is encrypted

## Slide 15: Wireless Network security
Tools to detect wireless devices
  Kismet (runs on Linux, available on Kali)
  Netstumbler (runs on Windows)
Tools to break encryption WEP, WPA, WPA2
  Aircrack-NG
  CoWPAtty

## Slide 16: Logs - Windows
Windows logs are categorized in to multiple logs.
  Application Log – Contains applications or program logs.
  Security Log - Contains valid and invalid login attempts.
  Setup Log – Contains events related to application setup.
  System Log – Contains events logged by Windows system components.
  Forward Events Log – Contains events collected from remote computers.
How to view the logs:
  Step 1: Go to Start button on Desktop task bar.
  Step 2: Select Control Panel.
  Step 3: Go to Administrative Tools -> Open Event Viewer
  Step 4: On left hand side of Event Viewer window, go to Event Viewer (Local) -> Windows Logs
OR
  Start  Run  eventvwr.msc

## Slide 17: Logs - Linux
Almost all logfiles are located under /var/log directory and its sub-directories on Linux.
Some examples
    /var/log/auth.log : Authenication logs
    /var/log/utmp or /var/log/wtmp : Login records file
    /var/log/maillog : Mail server logs
    /var/log/httpd/ : Apache access and error logs directory
    /var/log/boot.log : System boot log

## Slide 18: Redundancy
In a nutshell, redundancy in consumer-grade digital storage means using more internal drives than necessary to store the information, or in other words, storing the same data in more than one place. There are many ways to do this, but the most popular is the use of a type of RAID (Redundant Array of Independent Disks)
Redundancy is not a form of backup, but just a fail-safe measure in case of failure of the storage device's internal drive or drives.
You can think of redundancy as using two plastic bags, one inside the other, to carry groceries home from the market. This way, if one of the bags is broken or punctured along the way, food, especially broken eggs, won't spill out.
Read more at cnet:
https://www.cnet.com/how-to/digital-storage-basics-part-3-backup-vs-redundancy/

## Slide 19: Backups
Home users might not need redundancy but they definitely need backup, which basically means keeping separate copies of data in multiple places so that if something happens to one place you can turn to another. The more copies of data you have, the safer it is.
  Hard drive, USB thumbdrive, optical disks
Online backup (also known as cloud backup)
  Dropbox, Google Drive, SkyDrive, etc
In the same grocery shopping analogy, backup is like getting two (or more) separate bags of exactly the same groceries. In this case, if the eggs stored in one bag break, or even in the rare case that you dropped one of the bags and it was run over by a car, you would still be able to make breakfast the next morning thanks to the contents of the other bag.

## Slide 20: Incident Handling
Preparation
Identification
Containment
Eradication
Recovery
Lessons Learned
http://www.slideshare.net/namedeplume/frontline-solutions-for-security-practitioners-1008