## Slide 1: Internet and Networking Basics

## Slide 2: The Internet

## Slide 3: The “nuts and bolts” View
millions of connected computing devices:
  hosts = end systems
  Connected by
    routers and switches
communication links
  fiber, copper, radio, satellite

## Slide 4: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
  IXP: Internet eXchange Point
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 5: How a System/Device is Identified on the Internet: IP Addresses
Each computer connected to the Internet must have a unique address: IP (Internet Protocol) address
Internet addresses are in the form nnn.nnn.nnn.nnn where nnn must be a number from 0 - 255. This address is known as an IPv4 address.

## Slide 6: How many possible IP addresses are There?
256 x 256 x 256 x 256 = 4,294, 967,296
How many devices are connected to the Internet ?
More than 4.3 billion! 127 items per second according to an article at the NetworkWorld:
  http://www.networkworld.com/article/2942596/microsoft-subnet/127-devices-added-to-the-internet-each-second-but-congress-is-clueless-about-iot.html
  So IPv4 addressing scheme is not enough. IPv6 is the new scheme!

## Slide 7: IPv6
The next generation Internet Protocol (IP) standard intended to eventually replace IPv4.
IPv6 address has 128 bits:
Example: DE10:2D7B:0000:0CDE:1257:0000:211E:729C
(32 hexadecimal digits)
The number of potential IPv6 addresses has been calculated as:
340,282,366,920,938,463,463,374,607,431,768,211,456

## Slide 8: Domain Names

## Slide 9: DNS: Domain Name System
Mapping of (user-friendly) URL to IP address:
URL
IP Address
The Internet: IP Addresses and DNS by code.org

## Slide 10: What is your IP?
To find your IP you can do one of these:
http://whatsmyip.net/
OR
Click the START icon at the bottom left corner
  Type cmd in the text box
  When the window for command prompt appears, type ipconfig

## Slide 11: Networking and Protocols

## Slide 12: How files travel from one machine to another
Each file is broken into small packets
Each packet is like an envelope with content inside
Each packet contains source and destination addresses
Each packet travels through the Internet and goes from one machine to another via several routers

## Slide 13: How packets travel
Watch this video on how packets travel from code.org:
The Internet: Packets, Routing and Reliability

## Slide 14: Check It Out - The Ping Program
Ping is a software utility used to test the reachability of a host on an Internet Protocol (IP) network and to measure the round-trip time for messages sent from the originating host to a destination computer and back.
Click the START icon at the bottom left corner
Type cmd in the text box
When the window for command prompt appears, type
ping www.columbusstate.edu
Observe what happens

## Slide 15: Traceroute
Traceroute is a command which can show you the path a packet of information takes from your computer to one you specify. It will list all the routers it passes through until it reaches its destination, or fails to and is discarded. In addition to this, it will tell you how long each 'hop' from router to router takes.
In Windows, start the cmd prompt. Enter the word tracert, followed by a space, then the domain name.
Firstly it tells you that it's tracing the route to the destination, the IP address of that domain, and what the maximum number of hops will be before it times out.
Next it gives information about each router it passes through on the way to its destination.

## Slide 17: OSI Model
The Open System Interconnection (OSI) model defines a networking framework to implement protocols in seven layers. Control is passed from one layer to the next, starting at the application layer in one station, and proceeding to the bottom layer, over the channel to the next station and back up the hierarchy. http://www.webopedia.com/quick_ref/OSI_Layers.asp

## Slide 18: 7 Layers of the OSI Model

## Slide 19: OSI Layers at Work

## Slide 20: OSI Model and Protocols

## Slide 21: OSI Layers and Headers
Note that at each layer some header information is added to the data to let the other side know how to handle the packet.

## Slide 22: TCP Layer: Port Numbers
List of TCP and UDP port numbers
https://en.wikipedia.org/wiki/List_of_TCP_and_UDP_port_numbers
Common Ports Cheat Sheet (a copy is provided in the module)
http://mobinnet.ir/uploaded/common_ports.pdf

## Slide 23: Structure of a TCP/IP Packet

## Slide 24: TCP vs UDP Headers

## Slide 25: Wireshark
Wireshark is a free and open source packet capture tool and analyzer used for network troubleshooting, analysis, software and communications protocol development, and education.
You can download and read about wireshark at
https://www.wireshark.org/
In some of your Netlab assignments you will make use of wireshark to complete certain steps in the lab.