## Slide 1: Aseptic Technique

## Slide 2: Aim
To perform tasks in a manner which prevents microbial contamination of samples, equipment and the worker.

## Slide 3: Background
Microorganisms are ubiquitous
  They are too small be visible with the naked eye.
  Microbes grow in every conceivable environment – even inside us.
  Microbes can be moved through the environment by direct contact
  Microbes can be moved via air and water currents
  A specimen from the environment will rarely be pure.
Aseptic technique is to work without introducing contaminating microbes from the environment into your work area or work materials.
  It uses physical and chemical barriers to control the movement of microbes.
  Aseptic technique is used when acquiring a bacterial specimen from the environment and performing a bacterial transfer for culture/growth of an organism.

## Slide 4: Materials
Handwashing sink with soap
70% Ethanol
Bactcinerator
Disposable sterile transfer pipettes
Disposable sterile cotton tipped applicators
Sterile culture tubes
Sterile loop
Sterile broth and agar media
Tube rack
Biohazard bags and bins
Spill kit
Incubator

## Slide 5: Overview
This Photo by Unknown Author is licensed under CC BY
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA-NC
An aseptic work zone is generated using a heat source.
Bunsen burner
Bactcinerator.
Equipment is kept aseptic by heating (loops and the neck of culture tubes).

## Slide 6: Protocol
Aseptic zone
  An area approximately 12 inches square surrounding the heat source.
  Contaminating organisms will be carried upwards and out to the sides of the zone.
  The zone creates a physical (hot air) barrier which prevents ubiquitous organisms from entering a culture tube or petri dish while you work with it.
Cultures may be opened within the zone.
  Caps of tubes may be removed and the neck of the open tube heated by rotation at the heat source.
  This warms air at the neck so that it moves out from the tube and prevents organisms from moving in from the environment.
Petri dish lids may be removed quickly within the zone.
  No lid, cap or tool should be placed down on the bench.
  All culture manipulations should be performed while holding equipment in the zone.
Keep your aseptic zone tidy and organized
  Work with both hands moving things into the center of the zone without crossing back and forth
Keep tubes in tube racks – never let broth or a culture run into the lid

## Slide 7: Protocol
Loops and pipettes should be held like a pencil and always point in the downward direction when full with a culture, this prevents run off onto your hand.
Loops are sterilized by inserting into the heat source until the nichrome wire glows red (approx. 30s).
  The loop should be cooled for 30s within the aseptic zone to prevent heat from killing a bacterial sample that you wish to transfer.
A sterile object touched to a sterile object remains sterile.
If a sterile loop is used to pickup an organism it must be re-sterilized after transfer.
If a sterile disposable is used to transfer a bacterial culture it must be disposed of in a biohazard bag.
All spent cultures and used disposables must be disposed of though the lab waste management system.
  Biohazard bags for solid waste disposal (agar plates, pipettes, applicators culture tubes with small liquid volume, <5ml) via sterilization in the autoclave
  Disinfectant/decontamination pots with 10% bleach for large volumes of liquid waste >5 ml.

## Slide 8: Results
Working aseptically will ensure that sterile broths and media remain sterile prior to inoculation with your sample.
Working aseptically will ensure that your bacterial sample remains uncontaminated by ubiquitous environmental bacteria and fungi.

## Slide 9: Images
This Photo by Unknown Author is licensed under CC BY
Be organized – have everything you need in the aseptic zone.
This Photo by Unknown Author is licensed under CC BY-SA-NC
Keep culture caps, tubes and loops all in your hands within the aseptic zone as you manipulate the culture
This Photo by Unknown Author is licensed under CC BY-SA-NC
Flame the loop until it glows red. Cool before using to touch the culture

## Slide 10: Conclusions
Working aseptically will contain a microbial samples within a culture
Aseptic work uses sterile equipment which can not introduce contaminants to your specimen and cultures.
Surfaces are decontaminated using chemicals such as 70% ethanol
Hands are decontaminated by washing with soap and water
Loops are sterilized by heating
Disposable pipettes and applicators are sterilized by gamma irradiation and supplied wrapped to prevent contamination.
When manipulating a culture you must work close to a heat source so that ubiquitous organisms are prevented from “falling” onto your work by the raising heated air currents.
Only sterile tools (loops/Pipettes/applicators) should be used to transfer bacterial cultures from one growth media to another.
Growth media must be prepared and sterilized prior to use to grow culture samples.

## Slide 11: Application
Aseptic technique is applied in the microbiology lab for the manipulation of microbial cultures
Clinically, the introduction of medical devices to a patient must be performed in an aseptic manner
  No heat source
  Equipment is sterilized and gloves are worn to limit the introduction of microbes from the environment to the patient.
  Surgical equipment is sterilized before use.
  Clinic, hospital and surgical areas are sanitized to reduce exposure to microbial contaminants
  Repeated handwashing is performed.

## Slide 12: Troubleshooting
Organisms fail to grow after an aseptic transfer:
  You failed to allow the inoculating loop to cool before removing a sample
  The hot loop will kill bacterial cells it touches.
  You failed to touch the loop to your sample.
  You failed to resuspend the cells within your sample and removed only broth with the loop (remember that cells have mass and settle under the force of gravity).
Plates and cultures are visibly contaminated by fungal growth:
  You did not use a sterile loop for transfer
  You did not remove the culture lid, and rotate it in the heat source within the aseptic zone.
  When removing a sterile pipette or applicator from its package you touched the working end and contaminated it.