## Slide 1: Heat Fixed Smear

## Slide 2: Aim
To produce a thin layer of cells attached to a glass microscope slide for the use of staining and microscopic observation.

## Slide 3: Background
A smear is simply the spreading of a sample across the surface area of a microscope slide.
The goal of the smear is to distribute bacterial cells in a thin single cell (monolayer) layer across this surface.
A monolayer of cells will allow for accurate observation of cell morphology.
A monolayer will allow for stains to penetrate cells evenly.
The heat fixation step of the smear will “glue” cells to the surface so that they do not wash away during staining.

## Slide 4: Materials
Lens paper
Clean glass slide
Sterile loop
Fresh culture either broth or agar plate
Bactcinerator

## Slide 5: Overview
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 6: Protocol
Clean the slide with lens paper
Label the frosted region of the slide with the date and organism/sample name.
Aseptically remove 2-3 loopfuls of resuspended broth culture and touch them to the center of the slide.
OR…
Add 2-3 loopfuls of D.I. water to the center of the slide and then aseptically transfer 1 CFU to the water and gently mix the cells into the water.
Using a loop flat against the slide, spread the cell suspension slowly back and forth over the entire viewing surface of the slide.
Allow the smear to COMPLETELY air dry near the base of the bactcinerator.
Use slide tongs to hold the slide close to the opening of the bactcinerator – sample side away from the heat – for about 10 s.
Allow to cool completely.
The slide may be stored or stained as desired.

## Slide 7: Results
When observed under the microscope a monolayer of cells should be visible.
Cells will not wash off the slide during staining procedures due to the heat fixation of the smear.

## Slide 8: Images
This Photo by Unknown Author is licensed under CC BY-SA
https://pixnio.com/free-images/science/microscopy-images/staphylococcus-aureus/photomicrograph-of-spherical-cocci-gram-positive-staphylococcus-aureus-bacteria-magnified-250x.jpg
modification of work by Nina Parker https://openstax.org
SMEAR HEAT FIX OBSERVE MONOLAYER

## Slide 9: Conclusions
A heat fixed smear permits staining and observation of cell morphology and cellular arrangement.
  Cocci, bacilli, spirochete
  Clustering, chains, palisades

## Slide 10: Application
Fix fixed smears are produced for the following staining procedures.
  Simple stain
    Usually a single basic dye e.g. crystal violet, safranin, methylene blue
  Gram stain
    A differential stain using stains and counterstains

## Slide 11: Troubleshooting
Slide cracks during heat fixation:
  Smear was not completely air dried.
No cells are observed:
  Heat fixation was too short and cells were washed from slide during staining.
  Broth culture was not resuspended prior to removing cell sample.
  CFU from agar plate was not mixed to suspend cells on slide prior to spreading smear.
Cells are not in a single layer and are clumped or overlapping:
  Too many cells used to make the smear (> 1 CFU/ >2-3 loops of a turbid culture).
  CFU from agar plate was not mixed to suspend cells on slide prior to spreading smear.