## Slide 1: Gram Stain

## Slide 2: Aim
To differentiate bacteria on the basis of their cell wall structure.

## Slide 3: Background
Hans Christian Gram developed this staining procedure in 1884.
He wanted to be able to observe bacteria associated with disease.
  He stained bacteria such as Streptococcus pneumoniae in samples from pneumonia patients (Gram positive).
The Gram stain is an essential stain used to help identify bacteria.
The stain consists of a series of dyes added to a heat fixed smear of bacteria.
  Crystal violet, iodine, alcohol decolorizer and safranin counterstain.
Gram positive organisms stain purple because the thick peptidoglycan layer in their cell wall retains the crystal violet dye.
The alcohol decolorizer removes all of the crystal violet from the thin peptidoglycan layer in the cell wall of Gram negative organisms.
  These cells appear pink due to the safranin counterstain.

## Slide 4: Materials
Heat fixed smear of sample
Staining rack (plus tray or sink)
Slide tongs
Gram stain kit
  Crystal violet
  Iodine
  Alcohol decolorizer
  Safranin
D.I. or distilled water
Bibulus paper
Microscope
Immersion oil
Lens paper

## Slide 5: Overview
This Photo by Unknown Author is licensed under CC BY-NC has been modified.
Flood with crystal violet, 30 s
Flood with Safranin, 30 s
Wash with decolorizer
until it runs clear,
10-20 s
Flood with iodine mordant, 30 s
Wash with D.I. H2O
Wash with D.I. H2O
Wash with D.I. H2O
Wash with D.I. H2O
Use a heat fixed smear of a bacterial sample.

## Slide 6: Protocol
Use a heat fixed smear produced from a fresh culture or sample.
Place the slide, sample side up on a staining rack
Add crystal violet stain drop by drop until the slide has flooded
  Stain covers the entire sample but is held above it by surface tension.
  Stain for 1 min
Pick up one side of the slide with tongs or a gloved hand and hold it with a downwards angle.
Wash the surface gently with water starting at the top of the slide above the specimen.
  Continue to wash until all excess stain is removed and the water runs clear.
Lay the slide flat onto the staining rack.

## Slide 7: Protocol
Flood the slide drop by drop with the mordent iodine.
  Wait for 1 min. then wash as before with water.
Hold the slide at an angle and gently wash the surface with alcohol decolorizer for no more than 15 s.
  Immediately wash gently with water to remove all decolorizer.
Flood the slide drop by drop with safranin stain
  Wait for 1 min. then wash as before with water.
Blot the slide with bibulous paper and completely air dry before observing under the microscope under oil immersion with adequate illumination.

## Slide 8: Results
Gram positive cells stain purple
Gram negative cells stain pink

## Slide 9: Images
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-SA
https://pixnio.com/free-images/science/microscopy-images/gonorrhea-neisseria-gonorrhoeae/photomicrograph-depicts-the-gram-negative-bacteria-neisseria-gonorrhoeae.jpg
This Photo by Unknown Author is licensed under CC BY-SA-NC
SPIROCHETE COCCI BACILLI
GRAM POSITIVE
GRAM POSITIVE
GRAM NEGATIVE
GRAM NEGATIVE
GRAM NEGATIVE

## Slide 10: Conclusions
Gram stain differentiates bacteria into Gram positive and Gram negative groups.
The retention of crystal violet dye is the positive result for the staining procedure.
Crystal violet, a basic dye, stains the negatively charged cell wall & cell interior.
Iodine, a mordant, binds to crystal violet to form large insoluble complexes.
  this slows down the removal of the dye when the decolorizer is added.

## Slide 11: Conclusions
Alcohol decolorizer acts in the same manner on all cell types.
  It dehydrates the peptidoglycan layer, solubilizes lipids, (damaging cell membranes), and solubilizes the crystal violet complexes.
With a thin peptidoglycan layer the alcohol can penetrate the entire wall and allow crystal violet to be dissolved and rinsed out from the cell cytoplasm.
With a thick peptidoglycan layer the decolorizer cannot penetrate the distance into the cell interior quickly and release the crystal violet.
  This effect is TIME dependent i.e. if you decolorize for too long even a thick peptidoglycan layer will become so damaged that the crystal violet will rinse out.
Safranin, a basic dye, counterstains all cells pink. Gram positives look purple because purple is DARKER than pink. Gram negatives look pink because they are ONLY stained with Safranin.

## Slide 12: Application
Used at the start of the process to identify an unknown organism.
Used in clinical pathology labs to distinguish infections caused by Gram positive vs. Gram negative pathogens.
  Each group requires treatment with appropriate antibiotics.
  Some antibiotics cannot cross the G –ve outer membrane.
  G –ve infections should be identified quickly and treated to lower the risk of septic shock.
  Patient may die due to the inflammatory response to lipopolysaccharide on G -ve outer membrane.

## Slide 13: Troubleshooting
False positives and negatives:
  Use a fresh, actively growing culture of bacteria for the Gram stain. Cell walls become damaged in old cultures and give false results.
  Smear is too thick and overlapping cells look positive when they are negative.
  False positives are generated if decolorizer is not used for long enough
  False negatives are generated if decolorizer is used for too long.
Indeterminate color of stain:
  Magnification is too low
  Bright field illumination is too high (everything looks washed out) or too low (everything looks dark with poor contrast).
No staining:
  Bacteria without a peptidoglycan cell wall structure e.g. Mycoplasma sp., Chlamydia sp. and Rickettsia sp. cannot be Gram stained.
  Mycobacteria sp. resist Gram staining due to the waxy lipid mycolic acid in their cell wall structure.