## Slide 1: Wet Mount

## Slide 2: Aim
To observe microbes in their natural aqueous environment

## Slide 3: Background
A wet mount uses a sample from an aqueous environment such as a pond, river, fish tank or a broth culture.
The wet mount allows for microscopic observation of living organisms in contrast to stained specimens which are killed.
Organisms within the specimen are in their native form with respect to morphology and any cellular associations
If organisms are pigmented this may be observed
If organisms are motile this may be observed

## Slide 4: Materials
Clean microscope slide
Cover slip
Sterile transfer pipette
Lab tissue (Kimwipe)
Clear nail polish or mounting fixative (optional)
Microscope
Immersion oil
Lens paper

## Slide 5: Overview
This Photo by Unknown Author is licensed under CC BY-SA
Remove excess sample from around the coverslip
This Photo by Unknown Author is licensed under CC BY
Angle coverslip to expel air bubbles

## Slide 6: Protocol
Aseptically remove a sample of the liquid specimen using a sterile transfer pipette.
Add a couple of drops of sample to the center of a microscope slide.
  If available a concave well slide is designed to hold a larger quantity of sample
Discard any excess sample into a container with 10% bleach solution for decontamination.
Discard the transfer pipette into the biohazard waste bag.
Coverslip the sample by lowering first one side of the cover slip to the slide and allowing it to make contact with the sample.
Slowly lower the coverslip to cover the sample and exclude air.
Clean any liquid sample from around the coverslip with a Kimwipe.
  Dispose of wipe as biohazard
Seal the edges of the coverslip with a little clear nail polish (optional)

## Slide 7: Protocol
Place the slide on a microscope and focus at low power.
Find an area of the sample which contains a field of organisms.
Move to the x 40 objective, adjust the lighting, focus and observe.
Toggle the stage a little back and forth to view around the field.
If motile organisms move through the field move the stage to track them, whilst continually adjusting your focus.
  Remember that organisms are moving up and down through the sample and you will have to continually refocus.
You may increase magnification to x1000 using oil immersion if you wish to view prokaryotic cells.

## Slide 8: Results
Live microbes can be observed.
Cell morphology will be natural.
Motile and non-motile organisms will be distinguishable.
Pigmentation may be observed.

## Slide 9: Images
MIXED ALGAE: This Photo by Unknown Author is licensed under CC BY-NC
EUGLENA: This Photo by Unknown Author is licensed under CC BY-SA-NC
PARAMECIUM: This Photo by Unknown Author is licensed under CC BY-SA-NC
SPIROGYRA; This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-ND
DIATOMS
SPIROCHETES: This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 10: Conclusions
Wet mounts allow observations of live organisms.
Wet mounting preserves features destroyed by staining methods.
  Cell morphology may be altered during the heat fixation step required for staining samples.
Wet mounts permit observations for motility and pigmentation.
  Stained samples are dead due to heat fixation and thus can not be confirmed to be motile.
  Staining may mask any natural pigmentation.
Phase contrast or dark field microscopy may be used to observe wet mounts and improve contrast of the unstained organisms.

## Slide 11: Application
Use a wet mount when you wish to study features of an organism which are only observable when it is alive.

## Slide 12: Troubleshooting
Everything is moving is the same direction:
  This is not an observation of true motility. Organisms should be moving in different direction.
  If a wave of movement in one direction is observed, it is likely to be due to the thermal currents generated in the sample by the heating effect of the microscope lamp.
Organisms are moving too fast:
  Many organisms are fast and difficult to track.
  They may be slowed down by addition of methylcellulose to the sample.
  This is non toxic and increases the viscosity of the sample thus, slowing microbial motion.
I see a black line moving across the field:
  This is due to the sample drying out under the heat of the microscope lamp.
  The line is the retreating edge of your liquid drop.
The image is foggy:
  You did not remove excess sample which extruded out from the coverslip.
  The heat from the lamp will cause evaporation which can condense on the objective lens and cause fogging.