## Slide 1: Streak Plate
A.K.A. Quadrant streak plate

## Slide 2: Aim
To generate isolated colony forming units of bacteria

## Slide 3: Background
Bacteria growing in isolated colonies are considered pure.
Each colony is assumed to have grown from the a single parent cell which divided repeated by binary fission.
After 24 hours incubation a cell growing exponentially will have produced millions of identical daughter cells.
Millions of bacterial cells growing on an isolated area of solid medium (agar) are visible with the naked eye
Each colony is 1 colony forming unit (1 CFU).

## Slide 4: Materials
Sterile solid agar media in a petri dish
  usually a non-selective nutrient rich agar type e.g.
    Tryptic soy agar (TSA)
    Luria-Bertani agar (LB)
Aseptic work area with a gas Bunsen burner or electric sterilizer (Bactcinerator)
Inoculating loop
Sample of bacteria
  May be from a broth culture or growth on an agar plate
Sharpie to label plate

## Slide 5: Overview
1
1
2
1
2
3
1
2
3
4
Sterilize and
cool loop
Sterilize and
cool loop
Sterilize and
cool loop
Inoculate with sample
Streak and dilute
Streak and dilute
Streak and dilute
Streak and dilute

## Slide 6: Protocol
Working aseptically
Invert agar plate on the bench and label the bottom with initials/date/inoculum
Place bacterial sample for streak in the aseptic zone
STERILZE the inoculating loop and allow to cool.
Remove a loopful of inoculum from the broth or remove a small amount of growth from a plate
Lift the bottom or the sterile plate for the streak and inoculate a dime sized area close to the edge.
Gently drag the loop from the inoculum across the agar surface in a straight line (STREAK) at the top of the first quadrant.
Return to the inoculum site and perform three or more streaks parallel to, and below the original.
STOP. Replace the plate onto it’s lid.
STERILZE the inoculating loop and allow to cool.

## Slide 7: Protocol
Lift the streak plate and perform four parallel streaks across the second quadrant of the plate.
  Ensure that the first two streaks overlap with the end of the streaks in the first quadrant
    This will pick up cells and drag them into the second area of the plate
  The third and forth streaks should sit below the others but start further to the right.
    These will deposit the cells which remain on the loop and lead to an increased dilution effect.
STOP. Replace the plate onto it’s lid.
STERILZE the inoculating loop and allow to cool.
Lift the streak plate and perform four parallel streaks across the third quadrant of the plate in the same manner as before
STOP. Replace the plate onto it’s lid.
STERILZE the inoculating loop and allow to cool.
Lift the streak plate and perform two parallel streaks across the last quadrant of the plate, but this time continue the second streak as a zig zag towards the center of the plate.
Replace plate onto lid. Keep inverted and incubate overnight at an appropriate temperature.

## Slide 8: Results
Isolated CFU should grow in the third or fourth quadrant.
If the original sample contained a mixture of bacterial species multiple types of isolated CFU should be visible.
Observe carefully for different colony morphologies (color, margin shape, translucency etc.)

## Slide 9: Images
Isolated colonies in the forth quadrant of the streak plate

## Slide 10: Conclusions
The streak plate protocol is a method by which bacteria may be diluted across the solid surface of an agar plate.
Dilution using the entire area of the plate will result in individual cells being deposited in the last quadrant
Individual cells when incubated for 18-24 h will reproduce logarithmically resulting in millions of cells growing in the same spot.
The colony of cells will be visible by eye and is called a colony forming unit.
An isolated colony forming unit (CFU) is pure.
A CFU may be picked from the agar using a sterile loop and used to subculture a pure specimen of bacteria.

## Slide 11: Application
Streak plates are used to obtain isolated pure colonies of bacteria.
Pure colonies may be used to inoculate and grow pure cultures.
Streak plates may be used to separate isolated CFU from a mixed sample of bacteria.
Streak plates may be used to maintain pure cultures by periodically streaking and sub-culturing.
Streak plates may be performed on any type of agar media.

## Slide 12: Troubleshooting
No pattern of growth across the plate:
  Loop was not cool after sterilization between quadrants (this will kill the bacteria).
  You failed to enter the area inoculated in the previous quadrant and drag cells into the next quadrant (first two streaks).
  You lost track of where your quadrant streak ended (try marking the quadrants on the bottom of the petri dish and streak towards each line).
Too much growth and no isolated colonies:
  You did not sterilize your loop between each quadrant.
  You returned to the original sample and inoculated each quadrant instead of diluting.