## Slide 1: Selective and Differential Media

## Slide 2: Aim
Selective media contain reagents which produce a growth environment in which only certain types of organisms may grow well.
  The media places a selective pressure on growth
Many different selective media can be made to mimic the natural growth environments of different bacterial species.
Selective media are used to encourage the growth of specific types of organisms while inhibiting the growth of other organisms.

## Slide 3: Background
Selective media
Selective media are used to limit the growth of ubiquitous organisms within a sample and allow microbiologists to encourage growth of only a small group of related species.
The ability of an organism to grow on a particular selective media may also provide data for it’s identification.
Selective media supply defined nutrients which only some bacteria can metabolize
Selective media also contain reagents which create an environmental pressure which inhibits growth of some organisms but not others.
  e.g. high salt content or high pH.

## Slide 4: Background
Selective and differential media.
Selective media are often also differential for species within the selected group.
The differential nature of the media often uses a pH indicator.
  The pH indicator will visually demonstrate when an organism is metabolizing the media via a fermentation pathway.
  When acid is produced as a byproduct of fermentation the pH around the growing cells will be reduced.
Indicators are not a source of selection or nutrition

## Slide 5: Background
Differential media
Media may also be differential but not selective.
Blood agar is differential for species which can lyse red blood cells to obtain growth factors.
Blood agar is not selective as it is made simply by adding 5% sheep red blood cells to non selective nutrient agar.
The differential nature of the media is to detect organism which produce enzymes with hemolytic activity.
Hemolysis can be categorized as:
  β, complete destruction of RBC – clear zone
  α, partial destruction with green zone
  γ, no hemolysis, normal growth no zone

## Slide 6: Materials
Sample
Selective media broth or agar.
Non-selective control media
Sterile loop
Biohazard disposal
Bactcinerator
Incubator

## Slide 7: Overview
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA-NC
This Photo by Unknown Author is licensed under CC BY-SA-NC
ASEPTIC TRANSFER TO CONTROL AND SELECTIVE MEDIA.
This Photo by Unknown Author is licensed under CC BY-SA-NC
UNKNOWN SAMPLE
CONTROL AND SELECTIVE/DIFFERENTIAL MEDIA

## Slide 8: Protocol
Sample from broth culture
  Resuspend the sample
Sample from agar plate
  Pick an isolated colony
Aseptically transfer to the control media broth or perform a streak on an agar plate
Aseptically transfer to the selective media broth or perform a streak on an agar plate
Incubate the plate inverted/upside down, (to prevent condensation from dripping onto the plate) overnight at 25-37oC (depending on the temperature of the original sample).

## Slide 9: Results
Observe the control media for adequate growth (turbidity or growth along the streak line).
If adequate growth is observed proceed to observe results on the selective plate
  If growth is observed then the organism belongs to the group which the media is selective for.
  If no growth is observed on the selective media then the organism was inhibited and does not belong to the selected group of bacteria.
  If the media is also differential then observe for indication of a fermentation reaction.
If no growth is observed on the control plate the organism was not viable and the test must be repeated with a fresh sample.

## Slide 10: Images
This Photo by Unknown Author is licensed under CC BY-SA
Selective and Differential media
Mannitol salt agar contains salt which is selective for Gram positive Staphylococci sp.
Staphylococci sp. grow in sectors 2 and 3.
MSA is also differential on the basis of the ability to ferment mannose, as indicated by the color change.
  Sector 3, a fermenting pathogenic strain of Staphylococcus.
Growth of Gram negative E.coli is inhibited in sector 1.

## Slide 11: Images
This Photo by Unknown Author is licensed under CC BY
Selective and Differential media
MacConkey agar contains bile salts and crystal violet and is selective for Gram negative rods
It is differential for Enterobacteriaceae such as E.coli and Salmonella sp.
Differentiation is on the basis of the ability to ferment lactose in the media.
Staphylococci sp. grow in sectors 2 and 3.
A) Salmonella sp. Non-fermenting
B) E.coli fermenting
  reduces pH by acid production and changes pH indicator to Red

## Slide 12: Images
Differential media
Blood agar is differential but not selective
Detects hemolytic activity
Some gram positive cocci produce an type of exotoxin (hemolysin) which destroys red blood cells and hemoglobin
  e.g. Streptolysin of Streptococcus sp.
https://microbenotes.com/hemolysis-of-streptococci/

## Slide 13: Conclusions
Examples of selective/differential media:
Mannitol Salt Agar:
  Nutrient carbohydrate – mannitol
  Selective pressure - 7.5% sodium chloride
  pH indicators – phenol red (turns yellow below pH 7)
  Staphylococcus sp. Can survive at high salt concentrations and pathogenic strains ferment mannitol
    Remember different species and strains of organisms use different metabolic pathways.
MacConkey Agar contains:
  Nutrient carbohydrate – lactose
  Selective pressure – bile salts and crystal violet
  pH indicators – neutral red (colorless at pH 6.8 and turns red below pH 6.8)
  Used for differentiation of Enterobacteriaceae (enteric gut bacteria) e.g. Salmonella sp. and E.coli

## Slide 14: Application
For selection of a groups of organisms from a mixed culture.
For differentiation between related species of bacteria
For use in identification of unknown organisms.

## Slide 15: Troubleshooting
Adequate growth is not observed on the control plate:
  The test must be repeated with a fresh, growing culture from the original sample.
When inoculating sectors of a plate the differential color change spreads into a neighbor sector:
  Repeat with individual test plates for each organism.