## Slide 1: Kirby Bauer Test
A.K.A. Antibiotic sensitivity test via disc diffusion

## Slide 2: Aim
The antibiotic disc diffusion test (Kirby Bauer Test) is used, in conjunction with reference tables, to determine the susceptibility of an organism to standard concentrations of antibiotics.
Clinically, antibiotic susceptibility testing may then be used to provide guidelines to prescribe antibiotics for the treatment of a bacterial infection.

## Slide 3: Background
Antibiotics are naturally occurring compounds made by bacteria and fungi to defend against competition by bacteria in their environment.
Commercially produced antibiotics and related antimicrobials are used clinically for the treatment of bacterial infections.
Organisms which naturally produce antibiotic include members of bacterial Streptomyces sp., and fungal Penicillium sp.
Many antibiotics kill bacteria by interfering with cell wall synthesis which leads to a weakened structure and cell lysis due to osmotic pressure.

## Slide 4: Materials
Organism to be tested.
Antibiotic impregnated test discs
Muller Hinton agar plates of standard depth
McFarland standards for cell density
Sterile phosphate buffered saline (PBS)
Transfer pipette and sterile swab of cell spreader
Incubator
Bactcinerator for aseptic work
Biohazard waste disposal
Antibiotic susceptibility reference tables

## Slide 5: Overview
To perform an accurate susceptibility test all parts of the antibiotic challenge protocol must be standardized:
A standard number of bacterial cells must be plated for challenge 1.5x108 cells/ml.
Bacteria must be inoculated to produce a lawn of growth (no gaps between colonies).
Antibiotic impregnated discs of standard concentration and size must be used
Muller-Hinton agar must be used and poured in plates to a standard depth(4 mm) to ensure standard rates of diffusion through the agar.

## Slide 6: Protocol
Use a pure fresh culture of your bacterial sample.
Dilute in sterile PBS to a cell density equivalent to a 0.5 McFarland standard for turbidity.
Inoculate the agar plate to produce a lawn of growth by close swabbing in three directions.
Aseptically, place antibiotic discs onto the surface of the inoculated agar and gently tap in place.
Invert for incubation at 37oC for 18 H.

## Slide 7: Protocol
A standard cell density of organism must be challenged in the Kirby Bauer test. This cell density of 1.5x108 cells/ml is equivalent to the turbidity of a 0.5 McFarland standard.
McFarland standards contain a barium sulphate precipitate which produces a turbidity/optical density equivalent to a fixed number of resuspended bacterial cells.
The card placed behind the standard helps you determine if your sample culture matches in turbidity.
http://www.bioanalytic.de/en/product/article/mcfarland-bss-turbidity-standards.html

## Slide 8: Results
Measure the diameter of any zones around the antibiotic discs where growth of the bacteria has been inhibited.
Record this zone of inhibition as a diameter with units of mm.
Refer to reference tables, provided with the antibiotic discs, to determine if this size of zone categorizes the organism as sensitive, intermediate or resistant to each antibiotic tested.

## Slide 9: Images
Modified by Kenyon/Molesworth: This Photo by Unknown Author is licensed under CC BY
Lawn of growth
Zone of inhibition
Antibiotic disc

## Slide 10: Diffusion in agar
Time 0
15 mins 30 mins 45 mins 2 hours
24 h
Photo: Molesworth Kenyon 2023.
Images

## Slide 11: Conclusions
In general the bigger the size of the zone of inhibition the more likely the organism is to be sensitive to the antibiotic.
The Clinical Laboratory Standards Institute (CLSI) defines the standards for all clinical testing of antibiotics using the disc diffusion assay and publish the references for zone sizes associated with clinically used antibiotics.

## Slide 12: Application
The Kirby-Bauer disk diffusion susceptibility test is used in hospital labs to measure the sensitivity or resistance of bacteria in a patient sample to various antibiotics.
The results will help a physician to select an appropriate treatment against infectious bacteria.

## Slide 13: Troubleshooting
Lawn of growth is not produced on test plate:
  Inoculation was not performed with tight swipes of the swab
  Plate was not swab in three independent directions
  Bacterial sample was not diluted to the standard 1.5 x 108 cell/mL
Zones of inhibition overlap:
  Place fewer discs on the agar plate and move them further apart.
Discs fall off the plate during inversion:
  Tap discs gently but firmly onto agar surface.