## Slide 1: Chapter-02: Electricity

## Slide 2: Electric Charges
By gaining or losing electrons object becomes charged
Like charges repel and unlike charges attract one another
SI Unit of charge(q) is Coulomb (C)
Charge of an electron, e = 1.6 x 10-19 C
Conservation of charge Principle: electrical charge is not created nor destroyed, only transferred from one object to another
Charge is a quantized/discrete quantity
Charge on any object can be expressed as q = +/- (N) (e), where N is an integer and e is the charge of an electron

## Slide 3: Conductors and Insulators
Conductors are materials in which the electric charge move freely in response to an electric force
  - Copper, aluminum and silver
      - When conductor is charged in a small region, the charge readily distributed itself over the entire surface
Insulators are materials in which electric charges do not move freely
        - Glass and rubber
        - When insulator is charged by rubbing, only the rubbed area becomes charged

## Slide 4: Electricity
The rate of flow of charge is current
SI unit of current is Ampere
An ampere is the flow of one coulomb through an area in one second
Electric circuit: A path for current to flow from + terminal of a power source to – terminal of the power source
Current must have closed path (conducting path) to flow. If the closed path does not exist, current does not flow
The path for current flow is provided by conducting wires connecting a load/resister to the terminals of a power source (see picture a and b)

## Slide 5: Electricity
Current (𝐼) is the rate at which charge moves through a cross-section area 𝐴 of a wire
Positive charges move in the direction of conventional current
Current flows is in the direction opposite to the movement of negative charge
Current takes path of least resistance
Q) Charge flows through a light bulb. Suppose a wire is connected across the bulb as shown. When the wire is connected,
1) all the charge continues to flow through the bulb
2) half the charge flows through the wire, the other half continues through the bulb
3) Most the charge flows through the wire
4) none of the above

## Slide 6: Voltage (V) , Resistance (R) and Current (I) in a circuit
Voltage of a power supply: corresponds to the energy (work) needed to move a charge between the two terminals of the power supply
SI unit of voltage: volt
Voltage is created in a battery by electrochemical processes (e.g., cells and batteries)
Current/electricity: The rate of flow of charge through a medium
Resistance: The electrical resistance of an object is a measure of its opposition to the flow of electric current

## Slide 7: Voltage, Resistance and Current in a circuit
The black color zigzag symbol represents a resistor (R)
The red color parallel (long-short) lines represent a voltage source (V), aka power supply
Current (I) flows through the circuit
  - it starts from + terminal (long red line of power supply)
  - flows through black wires (conductors)
  - flows through resister (R)
  - flows back into the – terminal (short red line of power supply)
  Current coming out of the + terminal is equal to the current going into the
- terminal
The potential energy of the electrons is reduced as they pass through the resistor(s)
The voltage is dropped (consumed) as current flows through the resistor
In any circuit, voltage supplied by the power supply is equal to the voltage dropped (consumed) by the resistor(s)

## Slide 8: Resistivity and Resistance
Consider a uniform cylinder,
L: length
A: cross-sectional area’
Rho  : Resistivity is the property of substances that opposes electron flow through it
The longer the cylinder, the greater its resistance
The larger its cross-sectional area , the smaller its resistance.

## Slide 9: Ohm’s Law
Relationship between V, I and, R
Ohm’s law is not valid for all electrical materials or devices
Materials that obey Ohm’s law are referred to as Ohmic materials
    - e.g. resistors, conductors
    Materials that do not obey Ohm’s law are referred to as non-Ohmic materials
    - e.g.: diodes, capacitors, inductors etc.
Graphical form of Ohm’s Law
I
V
Simple circuit diagram
V

## Slide 10: Power consumption in a circuit
Electrical power (P) is the rate at which the electrical energy is transferred from voltage source and consumed by an electrical component (such as a resister R)
SI unit: Watt
Other formulae for Power:

## Slide 11: Current and Voltage measurements in circuit
An ammeter is used to measure current through a component. Its two terminals are connected in line with the component (in series). See Ammeter’s position in the image on right
A voltmeter is used to measure voltage. Its two terminals are connected to the two contacts of a component (in parallel). See Voltmeter’s position in the image on right.
An Ohm meter is used to measure resistance of a component. Its two terminals are connected to the two contacts of a component (in parallel). See Ohmmeter’s position in the image on right.

## Slide 12: Series and Parallel connections of components
Series connection of components
  In a series connection of two components, the output current of the first component (R1 resistor) flows into the input of second component (R2 resistor)
        The current is the same in each resistor but the voltage across them may vary (depending on the resistor value)
        Parallel connection of components
        All of the component terminals on one side (top side) are connected together and all the terminals on the other side (bottom side) are connected together
        In the case of a parallel configuration, all components have the same voltage across them, and the currents through each resistor may be different (depending on the resistor value)
Notes: https://openstax.org/books/university-physics-volume-2/pages/10-2-resistors-in-series-and-parallel

## Slide 13: Concept of Equivalent Resistance in a circuit
In an electrical circuit, the equivalent resistance (R_eq) is a single resistance value that is equivalent to all the resistors present in the circuit
For resistors connected in series,
    R_eq = sum of the resistances in the circuit
    Current through the series circuit,
    I = (V) / (R_eq) ( using Ohm’s law)
circuit with five resistors connected in
series
circuit with two parallel connected
resistors
Notes: https://openstax.org/books/university-physics-volume-2/pages/10-2-resistors-in-series-and-parallel

## Slide 14: Calculations using series connected resistors
Notes: https://openstax.org/books/university-physics-volume-2/pages/10-2-resistors-in-series-and-parallel

## Slide 15: Concept of Equivalent resistance in a parallel circuit
R_p = R_eq, equivalent resistance of R1 and R2 connected in parallel

## Slide 16: Other common components in circuits
Active components
  Add electrical power into a circuit
  Can also amplify electrical signals in a circuit
  Examples: power sources, transistors
Passive components
Consume power in the circuit
Cannot amplify electrical signals in a circuit
Examples: resistors, capacitors, inductors, and transformers
Electromechanical components
Carry out electrical operations by using moving parts or by using electrical connections
Examples: relays, actuators, motors
Notes: https://en.wikipedia.org/wiki/Electronic_component

## Slide 17: Capacitors
A capacitor is an electrical device that stores electrical energy in it by accumulating electric charges on its surface
It has two polar terminals + and –
SI Unit of capacitance: Farad (F)
Schematic diagram

## Slide 18: Inductor
Also known as a coil, choke, or reactor
Stores electrical energy only when electricity flows through it
Energy is stored in a magnetic field created by it
Typically consists of an insulated wire wound into a coil
Can be used to create electro-magnets
SI unit of inductance is the Henry (H)
Notes: https://en.wikipedia.org/wiki/Inductor

## Slide 19: Transformers
Used in transferring electrical energy from one electrical circuit to another circuit
Electrical energy can be transferred between two separate coils without a metallic (conductive) connection between them
Notes: https://en.wikipedia.org/wiki/Inductor

## Slide 20: LED: Light Emitting Diode
A passive device that emits light when current flows through it (like a bulb)
Made up of a semiconductor material
LEDs emit light as a result of electrons jumping from high energy levels to low energy levels in the semi conductor materials. This happens due to the flow of current through it
The color of the light is determined by the energy required for electrons jump between energy levels
Notes: https://en.wikipedia.org/wiki/Inductor

## Slide 21: Electrical switch
It is an electromechanical device
An electrical component used to disconnect or connect the conducting path in an electrical circuit
It can interrupt (start/stop) the electric current in a circuit
It can also divert flow of current from one portion of the circuit to another portion
Switch is "closed" means, both of its terminals are touching the circuit and electricity can flow between through the switch
Switch is "open“ means, both of its terminals are do not touch the circuit and electricity does not flow through it.
Notes: https://en.wikipedia.org/wiki/Switch

## Slide 22: Electrical Ground
Exposed conductive parts of electrical equipment are connected to the ground by wires, this is typically referred to as grounding
Grounding all electrical components is very important because it protect users from getting electrical shock
Electric shock: refers to the process where electricity (current) passes through a living body (person). It often results in tissue damage due to the heat generated by the passage of current through the body and is may be fatal
Grounding also stops the build-up of static electricity when handling flammable products or electrostatic-sensitive devices.
Before filling in gas in our cars, it is recommended to ground ourselves by touching the metal surface of the car. Else the static charge build in us may create a static spark and light up the gasoline
Notes: https://en.wikipedia.org/wiki/Ground_(electricity)